The Premier Waste UK facility is designed to receive non-hazardous and inert wastes and treat these wastes using physical processes to produce recyclable materials including Refused Derived Fuel (RDF). All activities take place within buildings that have automated dust and odour control mechanisms including fast opening and closing doors, good quality concrete floors and a sealed drainage system that controls any water produced within the system. Water collected is stored for use within the dust suppression system or reused within site processes. Mixed wastes are received and off loaded into the reception area from where segregation of non-hazardous and inert wastes takes place with particular reference to the segregation of gypsum based materials (plasterboard) for separate disposal as a single stream. Inert wastes are treated via screening to produce various recyclable materials that are then are stored separately prior to removal from site. Non-hazardous wastes are processed through a variety of screening and hand-picking processes to produce recyclable materials such as plastic, glass, wood and metal, which are then stored separately, with residual materials being re-sized through a shredding process and stored for onward transfer as RDF. Single stream wastepaper-pulp is received and processed separately for washing for the removal of plastic, with the resultant solid paper phase being returned to the producer, the plastic being processed with general waste on site and the water being reused within the process.  All external yard areas, none of which have contact with received or recovered wastes, discharge via a sealed drainage system and an interceptor (information provided by applicant) to sewer under a discharge agreement with Severn Trent Water. The sealed drainage system associated with the waste buildings is checked annually by CCTV inspection. The integrity of the site surfaces and drainage system is checked visually daily. There is a facility for the short-term secure storage of non-permitted materials received (quarantine). Buildings are constructed to minimise the effects of noise outside them and an automatic odour suppressant spray is activated whenever any of the buildings’ roller-shutter doors opens. Wastes are processed on a strict rotation based on when they were received to minimise potential for vermin and there is in place a contract with a pest control company. The ability of the site to address fires and the containment of fire water is addressed in the associated Fire Prevention Plan.

The application includes an extension to the permitted area to incorporate the area to the rear of the existing permitted area as shown on the Site Boundary drawing SAS/PRE/01. This area will remain non-operational until further notice.