Document 006  H1 Environmental Risk Assessment

| Farm Name: Ditchford Bank Farm Poultry | Applicant: G O Few and sons |
| --- | --- |

| Source of Emission | Emission (e.g. ammonia, dust, run-off, spillage, noise, odour) | Receptor (e.g. air, water, land, humans, plants) | Description of impact and duration of impact i.e. short term (ST), medium (MT) or long term (LT) | Significance of negative impacts Major +++ Moderate ++ Minor + Nil 0 | Mitigation / management measures for this emission |
| --- | --- | --- | --- | --- | --- |
| Poultry production (whilst houses are stocked and at clean-out) | Ammonia | Air Land Plants | Aerial deposition and direct toxic effect on trees (ST) Nutrient enrichment of soils (LT) Changes to sensitive ecosystems (LT) | +++ ++ +++ | Litter kept friable Feed formulated to match flock requirement Minimum ventilation programs |
|  | Dust | Humans Plants Land Water Air | Nuisance (ST) Contributor to odours (ST) Human health – inhalation (LT) Covers leaves, inhibits photosynthesis (ST) Nutrient enrichment of soils (LT) Nutrient enrichment of water courses (MT) Adverse effect on air quality (ST) | + + ++ ++ ++ + + | Use of suitable litter materials Use of pelleted feed delivered in sealed systems Litter is tipped into trailers from minimal height Trailers are covered when full Minimum ventilation programs |
|  | Dirty water (e.g. due to run-off during or after clean-out) | Land Water | Nutrient enrichment of soils (LT) Nutrient enrichment of water courses (MT) | +++ +++ | All dirty water is directed to sealed storage tanks Used litter spilt on roadways during clean-out is swept up |
|  | Noise | Humans | Nuisance (ST) | ++ | Measures as set out in Noise Management Plan |
| Poultry production (continued) | Odour | Humans | Nuisance (ST) | ++ | Measures as set out in Odour Management Plan |
|  | Zoonoses and notifiable diseases | Humans Livestock | Human and livestock health implications (ST) | + | Detailed biosecurity precautions in place e.g. frequent stock inspection, use of disinfectants and appropriate clean overalls, boots etc. for staff and visitors to prevent spread of disease |
|  | Feed (e.g. due to spillage from bins) | Land Water | Nutrient enrichment of soils (LT) Nutrient enrichment of water courses (MT) | + +++ | Feed bins are regularly checked for signs of damage and wear Feed bins are barrier-protected to prevent collision damage |
|  | Pests | Humans | Nuisance caused by vermin and flies | + | Pest control contractor visits monthly |
| Use of vehicles on site | Feed, used litter or dirty water (e.g. due to spillage from vehicles) | Land Water | Nutrient enrichment of soils (LT) Nutrient enrichment of water courses (MT) | + +++ | Any feed spillage beneath bins is cleaned up by driver Used litter is covered in trailers before leaving the site Machinery used to remove dirty water from tank is kept in optimum working order |
|  | Noise | Humans | Nuisance (ST) | ++ | Measures as set out in Noise Management Plan |
|  | Odour | Humans | Nuisance (ST) | + | Measures as set out in Odour Management Plan |
| carcass storage & disposal | Odour | Humans | Nuisance (ST) | ++ | Measures as set out in Odour Management Plan |
| Storage Facilities | Dirty water (e.g. due to overflow or leakage from underground collection tank) | Land Water | Nutrient enrichment of soils (LT) Contamination of surface and groundwaters (MT) | ++ +++ | Written procedures in place for monitoring tanks during clean-out. Appropriate staff have been trained |
|  | Fuels, disinfectants and other chemicals (e.g. due to spills or leakage) | Water Land | Contamination of surface and groundwaters with consequential effects on animals (ST) Contamination of land (MT) | +++ +++ | All storage tanks are bunded Smaller containers are kept in a purpose-built chemical store Environmentally-friendly products are used where possible |
| Storage Facilities (continued) | Health risks due to skin contact with stored materials, inhalation etc. | Humans | Human health issues (ST) | + | Accident management plan prepared and staff have received training COSHH data sheets for products used are kept on site Spill kits are readily accessible to contain spillage |

Appendix 1 – Pre Application Report Ammonia Screening