# Environmental Policy Statement

Our core business is Materials Recycling. This involves segregating, treating and the disposing of materials for recycling purposes. It is our aim to improve the local and global environment in which we operate, and to prevent pollution of the environment.

We are committed to compliance with all relevant legislation, regulations and other industry codes. As an integral part of this commitment, we will ensure that all emissions to water, land and air are within regulatory constraints and to strive to minimise the effect we have upon the environment through our commitment to continual improvement.

It is our policy to promote environmental awareness throughout the company and to ensure that operatives receive appropriate training relating to environmental issues.

Clients of Plasterboard Recycling Solutions Recycling will be made aware of the Company’s Environmental Policy.

It is an integral element of our policy to ensure open and clear communication of our objectives and achievements to all interested parties.

We have a commitment to monitoring our performance with regard to environmental issues, and the subsequent performance improvements. Regular objectives will be set and reviewed by Company’s management

Signed…………………………………….……Matthew Pearson, Plasterboard Recycling Group Ltd

# Introduction

This manual and associated Procedures represents the formal Environmental Management System (EMS) for Plasterboard Recycling Group Ltd.

This system has been documented to achieve and demonstrate sound environmental performance by controlling the impacts of the company’s activities on the environment consistent with our policy. The EMS supports compliance with the Environmental Permit operated at the site.

## Company Profile

Plasterboard Recycling Solutions recycling is a registered waste handler. The business operates from Smokes Lane, Chittening, Avonmouth, BS11 0YB. and operates predominantly as plasterboard recycling and storage facility but also limited metals and construction waste recycling site.

Site operating hours are as follows:

Monday to Friday:		0900 to 17.00;

Saturday:			0900 to 12.00; and

Sunday / Bank Holidays:	Closed.

## Scope of System

The scope of our environmental management system covers “The recycling of metals and other materials”.

The purpose of this manual is to define the EMS, which will ensure that the company activities are conducted in a manner which will minimise adverse environmental impacts and enhance our role in environmental stewardship.

The procedures that implement the EMS apply, where appropriate, to the company activities at Plasterboard Recycling Solutions Recycling and are operated under the same common management system.

## Environmental Risks and Effects

The company has identified and documented it’s Environmental aspects and Impacts below to identify the environmental aspects of the activities and determine those which have, or may have, a significant impact on the environment. Where necessary operational controls have been implemented to minimise any potential impact on the environment.

## Legal and Other Requirements

The key legislation and other requirements which establish the main environmental control over the company’s activities are defined within the Register of Environmental Legislation. Where appropriate, operational controls have been implemented to ensure compliance with relevant legislation.

## Environmental Improvement Programme

Objectives and Targets, with defined responsibilities for their monitoring, achievement and timescales have been documented:

Environmental Objectives will be established on an annual basis taking into account:

The Environmental Policy;

The significant environmental aspects based on the Risk Assessment;

Results of the Audits;

Legislative and other requirements; and

Views of relevant stakeholders.

## Operation & Maintenance

Operations and activities associated with environmental aspects are controlled by operational procedures referenced in this manual.

## Accidents and Incidents

The Company has established and maintains a procedure for incident and accidents in section 1.7 of this manual.

## Non-conformance, Incidents and Complaints

## The Company has established and maintains a procedure for recording Non-conformance, incidents and Complaints in section 1.8 of this manual

## Environmental Risk Assessment

The risk assessment below constitutes the typical risks present at Plasterboard Recycling Solutions Recycling in Avonmouth and identifies generic risks which are deemed to be applicable to the business activities of the company.

| Hazard | Receptor | Pathway | Risk management | Probability of exposure | Consequence | What is the overall risk? |
| --- | --- | --- | --- | --- | --- | --- |
| Smell from storage of waste . | Adjacent businesses on the industrial park | Air – South Westerly winds or lengthy periods of calm. | Ensure storage vessels are regularly checked and maintained in accordance with the procedures | Very low | Annoyance or nuisance to Adjacent businesses on the industrial park especially during warm summer months. Probably of limited duration. | Very low |
| Noise from the machinery on-site FLT’s etc | Adjacent businesses on industrial park | Air - Activities on site are potentially audible at other properties particularly gardens (no nearby residents) if any in the vicinity | Ensure activity undertaken in accordance with operating procedure Activity location benefits from being in an rural area with no residential properties nearby | Medium | Annoyance or nuisance to Adjacent businesses on industrial park especially during warm summer months. | Low |
| Spillages of liquids or contaminated rainwater runoff from metals storage or leaking from tanks or storage vessels | Groundwater | Indirect run-off through the soil layer, through current unmade ground. Sealed drainage system. Limited metals stored | Bunded, impermeable base in yard. Ensure regular inspections of impermeable surface and repair of damaged areas. Ensure regular integrity testing of storage vessels and drains. Regular inspections of bunds and tanks and waste storage areas. Storage area is hardstanding and drains to foul sewer. | Low | Contamination of groundwater | Low |
| Arson or vandalism causing the release of pollution material to air, water or land | Adjacent businesses on industrial park | Air transport of smoke or spillages and contaminated firewater by direct runoff form site. | Gates are closed and locked outside of office hours to block access further. Regular checks of the Perimeter and gates The premises is secured by fencing and earth bunds Only one entrance/ exit point to the site to/ from the public highway is in place, which is secured by means of lockable metal gates to be locked shut at any time the site is left unattended. | Low | Harm to health respiratory irritation Pollution of water via off site surface water drainage or adjacent land. Vandalism to oil storage areas | Low |
| Flooding of site | Adjacent businesses on | Flood waters | The site is in a floodplain but with good protection All storage vessels have secondary containment Ensure regular checking of and emptying of underground tank and interceptors. Ensure onsite drains are kept clear | Medium | If waste is washed off the site it goes to interceptor. | Low |
| Discharges to surface water from storage areas | Surfac e water and nearby drains | Overflow from main site into S/W gulleys in roads | Yard areas and gulleys will be checked on a monthly maintenance regime | Medium | Overflow or back up from the Interceptor | Low |
| Interceptor blocked and sitewater backing up | Interceptor discharges to surface water but if blocked could back up to yard | Overflow from main site to S/W gullies | Yard areas and gulleys will be checked on a monthly maintenance regime | Medium | Overflow or back up from the Interceptor to yard may enter S/W gullies on site | Medium |

## 1.4 Legal Register

| Legislation | Relevance | Applicable to which processes | Where held? | Person responsible for compliance |
| --- | --- | --- | --- | --- |
| The Scrap metal Dealers Act 2013 | Requires registration with the local authority as scrap metal dealer. | All scrap metal receipt, handling and dispatch | Copy held in site office | Owner |
| Environmental Permitting (Amendment) Regulations 2012 | The site requires an environmental permit to operate. Environmental permitting is a risk-based regime for regulating business activities that could have an impact on the environment or human health. | Storage, handling and treatment of waste on the site | Copy held in site office | Owner |
| Environmental Protection Act 1990 (Part II & Part III) | Defines the legal framework for duty of care for waste, and statutory nuisance. | The transfer of waste from site and the impact of operations on neighbouring residents. | Copy held in site office | Owner |
| Provision and Use of Work Equipment Regulations 1998 (PUWER) | Establishes requirements for those owning and controlling equipment used at a work’s premises | 360 | Copy held on site | Owner |
| Lifting Operations and Lifting Equipment Regulations 1998 (LOLER) | Establishes requirements for companies operating and owning lifting equipment | Lifting of material | Copy held on site | Owner |
| Health & Safety at Work Act 1974 | Establishes requirements for risk assessment for those working in potentially hazardous conditions | Working close to machinery Operating machinery | Copy held on site | Owner |
| Waste Framework Directive 2008/98/EC | Lays down controls for the safe disposal and recovery of waste. Article 13 lays down the objective that waste is recovered or disposed of without endangering human health and without using processes or methods that could harm the environment. | All site storage handling and treatment of waste on site. | Copy held in site office | Owner |
| Control of Pollution (Oil Storage) (England) Regulations 2001 | Applies where oils including (petrol, diesel, mineral oils) are stored on site in containers larger than 200 litres | Operation of equipment for materials handling on site | Copy held in site office | Owner |
| The Hazardous Waste Regulations 2005 ( as amended) | Ensures that Hazardous waste is tracked from the point of productions to the final point of disposal or recovery | Storage and transfer of specific wastes from those operations and which wastes cannot be accepted at site | Copy held in site office | Owner |
| The List of Wastes Regulations 2005 | Contains a harmonised list of hazardous and non-hazardous wastes | The operator needs to understand the properties of the wastes produced on site to ensure safe and secure storage and handling. | Copy held in site office | Owner |
| Waste (England & Wales) Regulations 2011 | Duty of care requirement s and information required on a waste transfer note | Handling, storage and transfer of Waste | Copy held in site office | Owner |

## 1.5 Site Objectives

Plasterboard Recycling Solutions Recycling Limited aims to operate in a way that minimises pollution to the local environment and does not pose a threat to any of our immediate neighbours by way of pollution, noise or disturbance. Further quantified objectives will be documented after the first year of operation of this EMS.

## 1.6 Operational Control

Plasterboard Recycling Solutions Recycling has developed a number of operational control procedures by which it undertakes its operations. These are listed here

- Firewater management –

- Noise management –

- Mud & Dust -

- Spills and incidents –

- Dealing with Floodwater –

- Plant & vehicle maintenance –

- Site Inspection & neighbourly relations –

- Drain & Bund checks –

- Site Plan –

- Sealed Drainage System -

- Material Processing –

- Waste Storage

## 1.7 Incidents and Accidents

The following table references other procedures and responsibilities in the event of an emergency situation

Reference to the appropriate procedure will give further guidance.

| No | Activity | Responsibility | Documentation |
| --- | --- | --- | --- |
| 1 | The following plan and associated supporting documents should be adhered to in the event of any of the following environmental accidents or incidents: Failure of storage tanks; Leak from oil storage tanks containment failure of bunds and impermeable surface; Spillages of waste oil, petrol and diesel during loading and unloading; Overfilling of vessels; Accidental fire causing release of smoke and fumes; Arson or vandalism causing the release of pollution material to air, water or land; and Flooding of site. | Owner and all members of staff | Spillage Response procedure; Fire Response Procedure; Accident and Incident Management Plan; Site Plan; Flood response Key Site and Emergency Contacts; List of PPE; and Accident and Incident Record. |

## 1.8 Incidents and Complaints

| No | Activity | Responsibility | Documentation |
| --- | --- | --- | --- |
| 1 | In the event of a complaint made to the site, the complaint record must be completed, and record kept | Owner | Complaint Record |
| 2 | Site Diary | Owner | Site Diary. A daily record of unusual or abnormal events will be kept in the form of a diary which will cover the whole site. |

## 1.9 Training & Awareness

Currently one member of staff is considered technically competent. They are Mr Matthew Pearson of Plasterboard Recycling Solutions who holds WAMITAB registration. They must ensure their presence on the site exceeds 35% of the working week.

The identity of site technically competent management has been made known to all site staff.

Management will make a record of training received by site staff, to be kept for as long as the person is employed at the site

More than one operative will be trained/ available to the site, so that holiday, sickness or other absence can be covered, allowing materials & metal recycling to continue in a manner that will not cause the site to become in breach of any licence or regulations condition relating to permitted activities. Training and Awareness of all requirements in the environmental permit and this EMS will be give to all staff within 6 months of grant of permit.

## 2.0 Management Review

Plasterboard Recycling Solutions Recycling will review and audit the contents of this EMS at no longer than yearly intervals. The review will take into account changes to the business, legislation and best practice. The system will be updated as necessary to drive continuous environmental improvement.