CLIMATE CHANGE RISK ASSESSMENT

Operators Name:	Morris Recycling Limited
Site Name:	Morris Recycling
Address:	Unit 34 Coneygree Industrial Estate, Tipton, DY4 8XP
Grid Reference:	SO 95764 90998
Permit No:	EPR/QP3725SW

Risk scoring matrix
Assess the impacts from each of the weather and climate change scenarios and calculate risk score using the risk scoring matrix.
The risk score is the likelihood of something happening multiplied by the severity of its impact.
	Severe impact (score 4)	Medium impact (score 3)	Mild impact (score 2)	Minor impact (score 1)
Highly likely (score 4)	16	12	8	4
Likely (score 3)	12	9	6	3
Low likelihood (score 2)	8	6	4	2
Unlikely (score 1)	4	3	2	1

Key: Risk categories:
12 to 16: high
8 to 9: moderate to high
4 to 6: moderate to low
1 to 3: low
Severity of impact:
- severe impact: short-term, acute impact to operations resulting in permanent compliance breaches
- medium impact: short-term, acute impact to operations resulting in multiple temporary compliance breaches
- mild impact: short-term, acute impact to operations resulting in single temporary compliance breach
- minor impact: short or long-term impact to operations resulting in additional measures for compliance
Likelihood:
- highly likely: event appears very likely in the short term and almost inevitable over the long term, or there is evidence of the event already happening
- likely: it is probable that an event will occur, or circumstances are such that the event is not inevitable, but possible in the short term and likely over the long term
- low likelihood: circumstances are such that an event could occur, but it is not certain even in the long term that an event would occur and it is less likely in the short term
- unlikely: circumstances are such that it is improbable the event would occur even in the long term

If the pre-mitigation risk score (column D) is 5 or higher, columns E to H must be completed.

Potential changing climate variable	A / Impact	B / Likelihood	C / Severity	D / Risk / (B x C)	E / Mitigation / (what will you do to mitigate this risk)	F / Likelihood / (after mitigation)	G / Severity / (after mitigation)	H / Residual risk / (F x G)
Summer daily maximum temperature / This may be around 7°C higher compared to average summer temperatures now, with the potential to reach extreme temperatures as high as over 40°C with increasing frequency based on today’s values.	Potential for increased waste reactions or fires involving heat sensitive or combustible waste.	1 / Window frame waste and PVC is not heat sensitive and uPVC is inherently flame-resistant and won’t start, sustain, or promote the growth of a fire.	1	1	Not required
	Potential for fire if the temperature exceeds the heat rating of components in electrical equipment or components are subjected to intense and direct sunlight.	1 / All electrical equipment in buildings	2	2	Not required
	Potential increase in high temperature expansion and stress of plant, pipework and fittings. UV degradation of plastic pipes and hoses causing them to fail.	1 / All pipework in buildings	1	1	Not required
	Potential increased dust emissions from processing areas, stockpiled material and site roads. Reduced availability of water for dust suppression.	1 / Window frames and profiles are not dusty waste. / No external processing areas / No site roads	1	1	Not required
	Long periods of hot and dry weather could lead to a drought and may have an impact on water supplies for:	1 / No processes that require water / External hydrants used	1	1	Not required
	Potential increased risk of pests and scavengers from stockpiled waste	1 / Window frames and PVC does not attract pests	1	1	Not required
	Potential increased risk of wildfires impacting the site.	1 / Site on industrial estate with no trees or vegetation surrounding site	1	1	Not required
Winter daily temperature / This could be 4°C more than the current average with the potential for more extreme temperatures, both warmer and colder than present.	Slightly higher winter maximums could generate regular odour complaints and pest infestations.	1 / Window frames and PVC does not attract pests and not odourous waste	1	1	Not required
	Lower winter temperatures could result in an increased risk of pipes (or similar) freezing.	1 / All pipework in buildings	1	1	Not required
Daily extreme rainfall / Daily rainfall intensity could increase by up to 20% on today’s values.	Potential for increased site surface water and flooding.	1 / Site not in flooding area and yard and buildings elevated from road where surface water runs.	2	2	Not required
	There is potential for drainage systems and interceptors to be overwhelmed.	2 / Drainage systems are inspected and maintained / Site drainage system and interceptor has sufficient storage capacity	2	4	Not required
Average winter rainfall / Average winter rainfall may increase by over 40% on today’s averages.	Potential for increased site surface water and flooding.	1 / Site not in flooding area and yard and buildings elevated from road where surface water runs.	2	2	Not required
	There is potential for drainage systems and interceptors to be overwhelmed.	2 / Drainage systems are inspected and maintained / Site drainage system and interceptor has sufficient storage capacity	2	4	Not required
Sea level rise / Sea level rise which could be as much as 0.6m higher compared to today’s level.	If a site is located near the coast there is potential increased risk of flooding.	1 / site not near the coast	1	1	Not required
Drier summers / Summers could see potentially up to 40% less rain than now.	Long periods of hot and dry weather could lead to a drought and may have an impact on water supplies for:	1 / No processes that require water / External hydrants used	1	1	Not required
	There is potential increased impact of discharge to watercourse from on-site drainage systems where connected to water courses.	1 / Discharge to surface waters from yard area only. Drier summers would not increase run off from yard areas.	1	1	Not required
7. River Flow / The flow in the watercourses could be 50% more than now at its peak, and 80% less than now at its lowest.	Increased impact from on-site drainage systems where they are connected to watercourses.	2 / Receiving waters 480m from site.	2	4	Not required
8. Storms / Storms could see a change in frequency and intensity. The unique combination of increased wind speeds, increased rainfall, and lightning during these events provides the potential for more extreme storm impacts	Potential for high winds to damage buildings and infrastructure and blow waste from the site.	1 / Window frames and profiles are heavy waste and would not blow / External walls would help to contain any infrastructure that may blow	2	2	Not required
	Potential for high winds to cause problems with stability of above ground storage tanks on jacks. This poses a risk to staff, plant infrastructure and the potential to release the contents of the storage tank.	N/A on this site