Non Technical Summery

| Farm Name: Weavers Meadow Pig Unit | Applicant: Crealy Farms |
| --- | --- |

Date:  02 September 2022

Prepared by:  Harry Edwards, The Farm Consultancy Group and Mr Chris Down

Weavers Meadow Farm will have a capacity for:

Sows and Farrowers: 1771

Pigs 7-15 kg – 1460

Production Pigs above 30kg – 432

The site is run as a fully slatted or part slatted based system with vacuum slurry removal, the existing housing and the proposed housing to all be operated as per BAT with frequent slurry removal.

A BAT assessment has been carried out for both the existing pig buildings and the proposed new building. This BAT assessment has not identified a need for an improvement program based on the buildings utilising biofilters.  As the existing buildings are built to the same specification as the proposed new building both of which are to comply with BAT AELS.

The majority of buildings are ventilated using variable spend roof fans with some buildings operating natural ventilation. Slurry is collected underneath the buildings and pumped out at least every 12 weeks to ensure slurry depth is maintained below 800mm.

The unit operates a mostly dry feed system, the diets fed to all the pigs throughout all stages are balanced nutritionally and formulated in such a way to minimise the production and emissions of ammonia, odours, dust and the overall environmental impact of the farming activities.

Nipple drinkers are used throughout to prevent water wastage. Meter readings will be taken on a regular basis to monitor water consumption and to detect the presence of any leakages, the site utilises borehole water and has mains water as a backup.

All lorries are washed out and disinfected regularly, maintaining cleanliness to a high standard. Each lorry is equipped with a shovel, bag and brush for instant clean up of accidental spillages, thus reducing emissions of both dust and odour.  Washings are captured and drain back into the contained slurry system.

These measures are intended to reduce the production and emission of ammonia odours and to prevent dust and liquids escaping into the environment. The batch system enables the housing to be cleaned out on a regular basis, ensuring all pig housing is as clean as possible. All dead stock will be disposed on via on site incineration.   Data sheet in appendix 1.