FIRE RISK

ASSESSMENT

AT

OATES ENVIRONMENTAL LTD

10 Carr Crofts Drive

LEEDS

LS12 3AL

DATE: NOVEMBER 2022

(REVIEW: NOVEMBER 2023)

## FIRE RISK ASSESSMENT

STEP 1 - IDENTIFY SIGNIFICANT FIRE HAZARDS IN THE WORKPLACE

Sources of ignition and their location: Warehouse: Lighting Electrical cutting equipment Hot washer Fork Lift Truck Plant Room (Warehouse): Various electrical equipment Laboratory: Various electrical equipment Canteens: Microwave, Toaster, Sandwich Toaster etc. Office: Various Office Equipment

Sources of fuel and their location: Waste Storage Bays (Warehouse): Various Flammable solid / liquid waste(s) Laboratory: Various Flammable solid / liquid waste(s) Diesel Storage Tanks (Warehouse & Yard): Road & red diesel Aerosol/ Gas Store: Various waste aerosol canisters LPG Bottles Yard: Wood Pallets Offices: Small amounts of paper, cardboard, office waste etc.

Sources of Oxygen and their location: General Ventilation + 2 Roller Shutter Doors / 4 roof extractors, Laboratory & Office windows

STEP 2 - DECIDE WHO COULD BE HARMED

People at Significant Risk: Employees, Visitors, Delivery Drivers etc.

How will they be Warned: Verbal warnings & activation of Hard-Wired Break Glass Alarm System

How Will they be Evacuated: Through numerous Fire Exits and then to assembly point – Front Gate Entrance (A). Alternative escape routes could be the Roller Shutter Doors if others are blocked by fire etc. Visitors, Delivery Drivers etc. are accompanied at all times and escorted to the exits in the event of a Fire.

STEP 3 - EVALUATE THE RISKS (ARE EXISTING MEASURES ADEQUATE)

Control of Ignition Sources / Sources of Fuel: Flammable liquids / solids stored in segregated bunded areas with Fire Block Walls, Fire Suppression & secondary containment Aerosols & Gas Canisters stored within a ventilated store with missile protection & Fire Suppression. General waste placed in skips/ bins & removed on a regular basis Wooden Pallets stored outside away from ignition sources All electrical equipment serviced in accordance with manufacturers recommendations etc.

Are these controls adequate? YES

What else needs to be or can be done? Regular daily Fire Watch site monitoring/ inspections

Fire Detection Methods/Times and Warning in the Area: Hard wired Break Glass Alarm System Various warning signage

Are these controls adequate YES

What else needs to be or can be done? Smoke Detectors within the warehouse & offices linked to the Break Glass Fire Alarm

Means of Escape and Signage in the Area: Numerous Fire Exit Doors within the Warehouse waste store, Laboratory & offices etc. The Warehouse has 2 open Roller Shutter Doors. Fire Exit Signs are being displayed. Emergency lighting throughout

Are these controls adequate YES

What else needs to be or can be done? Nothing at this time

Maximum Travel Distance to Safe Place and Estimated Evacuation Times: Maximum travel distance would be from the upstairs office; however, it should be noted that this area is used for only 8 people. There are numerous exits from the building which contains plenty of open space so if routes to exits are blocked alternatives could easily be found. The Warehouse waste storage areas are not large enough to have Travel Distance or Times that should be of major concern.

Are these controls adequate YES

What else needs to be or can be done? Nothing at this time

Fire Fighting Equipment / Measures located in the area: Each area has a combination of CO2, Powder and Foam Extinguishers in numerous positions throughout the premises and in warehouse areas as well as hallway, canteen, office etc areas. Flammable Waste Storage Bays have over 2m high Fire Block walls & Fire Suppression This provides cover for the type of fires that could occur in the premises.

Are these controls adequate YES

What else needs to be or can be done? Nothing at this time

Arrangements for Maintenance and Testing of Fire Precautions: Alarms: Will be tested and serviced every year. Emergency Lighting: Will be tested and serviced every year were applicable. Fire Fighting Equipment: Annual Service Contract Means of Escape: Exits are unlocked every morning, No Formal Procedures. Signage: Illuminated signage will be tested.

Are these controls adequate YES

What else needs to be or can be done? Keep records of any tests or inspections that are carried out.

Fire Procedures and Training for Employees: Fire Procedures have been developed and basic ones are on display in some areas, formal training is to be given to employees regarding this. Fire procedures are included in the induction process.

Are these controls adequate YES

What else needs to be or can be done? Toolbox talks on procedures to be carried out with staff were & when applicable

Arrangements for Disabled People: No current employees are disabled. Any visitors with disability are accompanied at all times and escorted to a place of safety in the event of fire.

Are these controls adequate YES

What else needs to be or can be done? In the event that any one is employed with a disability the fire procedures etc. will be fully reviewed to take the disability into account and where necessary additional measures will be put in place.

Other Practical Measures: Ensuring Good Housekeeping: Ensure rubbish is cleared away. Ensuring Escape Routes are kept clear: Documented Daily Fire watch Security Measures to Prevent Arson: Units are locked at night, CCTV

Are these controls adequate YES

What else needs to be or can be done? Nothing at this time

| STEP 4 – ACTION PLAN FOR IMPROVEMENTS REQUIRED |
| --- |
| Action Required | Person Responsible | Target Date for Completion |
| Waste Storage Review Removal of Waste Regime Check Fire Exits/Routes Fire Drills Service Fire Equipment Record Keeping Check Emergency Lighting Fire Emergency Plan to display | Francis Tebbutt / S. Oates Francis Tebbutt / S. Oates Francis Tebbutt / S. Oates Francis Tebbutt Francis Tebbutt Francis Tebbutt Francis Tebbutt Francis Tebbutt | Ongoing Ongoing Ongoing Ongoing 12 Monthly. Ongoing Visual daily. Completed |
| STEP 5 - REVIEW AND REVISE – NOVEMBER 2023. |