Noise Management Plan

CONTENTS

1.	INTRODUCTION	1

Roles and Responsibilities	1

Site Description	1

Site Plan	2

2.	SOURCES, PATHWAYS, RECEPTORS	2

Source Materials - Inventory	2

Pathways	3

Receptors and Wind Direction	3

3.	PRIMARY NOISE CONTROL MEASURES	4

Noise Releases	4

Impacts	4

Management of Releases	5

4.	Monitoring & Trigger Levels	6

Introduction	6

Communication	7

Complaints procedure	7

5.	Incidents and Emergencies	8

Appendix A  Site Plan – draft	9

Appendix B Noise Survey Form	10

Appendix  C Noise Complaint Form	12

INTRODUCTION

This document provides the Noise Management Plan prepared in accordance with

Environment Agency Guidance in support of environmental permit application

EPR/KB3503FK/A001

  - It relates to the inert waste transfer station operated by Fastlay Services Limited at Windy Bottom, Sittingbourne Rd Detling, ME14 3ES.

The operation will include the storage & manual sorting of inert C&D waste only.

The overall responsibility for this procedure is the Environmental Manager.  The Environmental Manager will be responsible for ensuring that all staff are trained in this procedure.

  - The Site Manager is responsible for ensuring that the day-to-day operations are carried out in accordance with this procedure.

  - All staff are responsible for implementing this procedure and have a duty to carry out their roles to prevent noise emissions.

## Site Description

  - The site is located at ME14 3ES on the Sittingbourne Rd, just north of the M20. It is a rural industrial estate surrounded by woodland and agriculture with few residential neighbours. It is approximately 3Km NE of Maidstone.

## Site Plan

  - A basic site layout is provided in Appendix A.

  - The company Environmental Management System (EMS) will be updated and revised accordingly as a living document as environmental and noise management develops

SOURCES, RELEASES, IMPACTS

  - This section sets out the protection sources of noise, potential release points and receptors.

## Source Materials - Inventory

  - Given the operations, it is considered that the activities which are most likely to give rise to noise are those in Table 2.

| Activity | Description | Comments |
| --- | --- | --- |
| Waste Delivery into covered bays | Delivery of waste nto the covered firebays on the east side of the site | Managed and timed |
| Vehicle movements | Movements of material onto and off of site | Managed and timed |

Table 2 Source Activities

  - It is anticipated that the likelihood of noise being emitted from these activities is medium/low on delivery or movement.

## Pathways

  - The pathways by which the noises from the sources identified above may impact upon a receptor are primarily:

1.  Air Movement of noise through air, particularly relevant on a site which will load/unload outside.

2. Direct exposure.  Particularly for staff, they will be exposed immediately to any noises from the product handling on site.

## Receptors and Wind Direction

  - The site is on an industrial estate which means key receptors sensitive

to noise are staff and immediate residential properties nearby.

  - The nearest residential properties are bordering the site to the NW. These are owned by the site operator.

  - The key receptors are shown in Figure 1.

The prevailing wind direction in the area, where the site is located, is South-Westerly.

Figure 1: Site and Key Receptors

PRIMARY NOISE CONTROL MEASURES

  - The control measures set out in this NMP are commensurate with the medium noise potential for the operations, in accordance with the statement to this effect in H3 Guidance

  - Noise can only cause an impact when it is perceived at a receptor site. This NMP has identified that the key opportunities for release of noises are anticipated to be:

1. When waste is delivered to site and removed.

2. When waste is loaded and unloaded.

3. When the manual sorting process occurs.

## Impacts

  - The impacts of any noises released as a result of Fastlay Services Limited’s activities will be linked to the receptors identified in Section 1.

  - The receptors are more likely to be impacted upon by noise in the following conditions:

- Prevailing wind direction is towards receptors; and

- Local weather conditions. Warm still weather will contribute to the perceived  noise at receptors including staff on the industrial estate, school children and residents.

- Cumulative impacts.   It is anticipated that cumulative impacts will be minimal.  The site is not in an area dominated by facilities which may cause additional noise.

  - The impacts of noise from the site are anticipated to be minimal, given the nature of the operation and the location within an rural setting. However, this will be confirmed regularly with monitoring and communication with neighbours.

## Management of Noise

  - If noise monitoring or complaints indicate a problem, Fastlay Services Limited will respond appropriately.  Management measures to control releases will include:

- Reducing the loading/unloading time on site.  As part of the site’s Management System, information on the loading/unloading on site will be recorded via operations, including arrival time on site. Minimal handling will ensure that noise is not exacerbated.

If the Site Manager deems that noise is causing a disturbance, the Site Manager will log this as an incident, using the appropriate forms from the Management System and will take corrective action

The site management will liaise with the contractors/hauliers and transport contractors, with a view to minimising the storage and transport periods for vehicle movements;

- Unanticipated noises. Any unexpectedly noise shall be recorded as to composition, date and time received and cause of noise

- Timing of loading/unloading. Site Manager observes that the prevailing wind direction is will not create noises towards the direction of sensitive receptors or when winds are light and noise will be reduced.

- Containment and abatement.  Given the nature of the operations on site, it is not considered necessary to implement containment and abatement techniques, other than those mentioned in the noise report. However, this is a ‘live’ document and as such will adapt if noise issues arise which are not managed by the actions in this NMP.

Monitoring & Trigger Levels

## Introduction

  - To ensure that the noise control measures set out in Section 3 are being effective, Fastlay Services Limited will ensure noise monitoring is in place and communication with potential receptors is maintained.

  - The following monitoring activities are regularly undertaken to ensure continuous improvement:

- Site inspections by the site manager (as outlined below)

- Site audits conducted by the company’s management;

- Site audits and inspections by the Environment Agency.

  - All site personnel will be responsible for reporting any noise problems immediately to the site manager (or deputy).

## Noise monitoring

  - The Site Manager will ensure that regular inspections are made of the site and its perimeter in order to identify any sources of noise and to establish whether any noise is discernible at the perimeter and thus likely to impact upon receptors.

  - In the event that noise is detected at the site boundary, additional monitoring will be undertaken at the sensitive receptors in accordance with Appendix B.

  - An auditory test will also take place in response to complaints.  The surveyor will undertake the survey at the location of the complaint and at potentially sensitive receptor locations in the vicinity downwind from the site.  At each location observations are made concerning the intensity of the noise, its persistence and character (these details will be logged in the pro forma, see Appendix C).

  - The surveyor may be the site manager or alternatively a staff member from the office or external person who is not used to the noises on the site.

  - Trigger Levels. If noise is detected at the assessment location and is judged to be a moderate or unacceptable noise, as defined in reference Table A - Appendix B, then the Site Manager and Management Team will be informed immediately and corrective actions will be determined and implemented.

  - Monitoring Frequency will be in accordance with Table 3

| Technique | Frequency |
| --- | --- |
| Noise Monitoring / Auditory Testing | Weekly at site perimeter. Noise detection will lead to receptor monitoring. Increase frequency in response to complaints |
| Complaints system | Continuous (24 hours) via telephone reporting system to Environment Agency Direct complaints to site in operational hours |

Table 3 Monitoring Frequency

## Communication

  - Liaison with neighbours.  If noise is anticipated on site or weather conditions predicted indicate noises will increase, the Site Manager will liaise with neighbours and ensure they are aware of the situation, how long it is expected to last and how to make a complaint.

  - Signboard. The site will have a legible signboard giving contact details for the Environment Agency and the operator.  These numbers can be used in order to make a complaint.

## Complaints procedure

  - All complaints, whether direct from people in the neighbourhood, or via the Environment Agency will be treated seriously by Fastlay Services Limited and recorded in the Noise Complaints Form in Appendix C.

Trigger Levels.  Fastlay Services Limited recognise that persistent noise can be a concern for neighbours and particularly for residential areas.  Every complaint is a trigger for management to take action to investigate the cause of a complaint, as set out in the Noise Complaints form.

Incidents and Emergencies

  - This section of the NMP relates to potential incidents or emergencies which may impact on the ability of Fastlay Services Limited to control noise from its site.

  - Potential incidents which may impact on noise are outlined as follows:

| Potential Incident | Actions |
| --- | --- |
| Unexpected noise in loading or unloading | The Site Manager will: Communicate with local receptors on expected duration if excessive. Record start/stop timings Record the incident in the site diary and using the appropriate management system forms and records. |
| Low wind/still conditions | If noise monitoring detects a problem, the site manager will: Ensure handling is kept to a minimum Record the incident in the site diary and using the appropriate management system forms and records. |
| Unexpected noise during out of hours. Unlikely. | The site manager will Investigate the cause of the noise Identify if it can be rectified immediately Notify local receptors as soon as practical Records the incident in the site log |

Appendix-A

Appendix B Noise Survey Form

| Noise Survey Recording Form | Reason for Noise Survey | Noise detected at boundary? Y/N Complaint Y/N Other |
| --- | --- | --- |
| Name of Surveyor |  | Job Title |  |
| Date |  | Time of Survey Start/Finish |  |
| Air Temp. oC |  | Wind Direction |  |

Survey Results

| Location | Noise Intensity See Reference Table A | Noise Extent See Reference Table B | Description of noise e.g. intermittent, ongoing? |
| --- | --- | --- | --- |

Reference Table A: Noise Intensity

| Noise Intensity | Description |
| --- | --- |
| 1 | No detectable noise |
| 2 | Faint noise (barely detectable, need to stand still and look into wind) |
| 3 | Moderate noise (noise easily detectable while walking, possibly offensive) |
| 4 | Loud noise (bearable, but offensive noise) |
| 5 | Very loud noise (this is when you really wish you were somewhere else) |

Reference Table B: Noise Extent

| Noise Extent | Description |
| --- | --- |
| 1 | Local and not persistent (only detected during brief periods when wind drops or blows) |
| 2 | Not persistent as above, but detected away from site boundary |
| 3 | Persistent but fairly localised |
| 4 | Persistent and pervasive up to 50m from site boundary |
| 5 | Persistent and widespread (noise detected >50m from site boundary) |

Appendix  C Noise Complaint Form

| Complainant Details |
| --- |
| Time and Date of Complaint |  |
| Complainant Name & Address |  |
| Complainant Phone Number/ Email address |  |
| Noise Details |
| Date noise noticed |  |
| Time noise noticed |  |
| Location of noise (if not address above) |  |
| Wind Direction (e.g. From South West) |  |
| Complainants Description of Noise: |
| -What does it sound like |  |
| -Intensity (see reference Table A, Appendix B) |  |
| Duration – how long was it detected for |  |
| Constant/intermittent in this period |  |
| Complainant comments/observations |  |
| Additional Information |
| Are there other complaints from this area? |  |
| Is the site the likely source of noise? |  |
| What was happening on site when the noise occurred? |  |
| Corrective Actions |
| Actions Required |  |
| Deadline for Actions |  |
| Person Responsible for implementing actions |  |
| Form completed by -Name and Role |  |
| Date |  |
| Signature |  |

# Footnotes

H3 Horizontal Guidance Noise Management (IPPC H3 part2)

http://www.metoffice.gov.uk/climate/uk/regional-climates/so