| Source | Pathway | Receptor | Harm | Likelihood | Consequence | Magnitude of Risk | Justification of Magnitude | Risk Management | Residual Risk |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Release of particulate matter (dusts) and micro-organisms (bio aerosols) | Atmosphere and then inhalation | Local human population & Site staff | Harm to human health (respiratory irritation and illness) | High | High | Medium | Permitted wastes do not include wastes that solely consist of dusts, powders or loose fibres Shredding of waste wood has the potential to cause dust | Regular maintenance of all hardstanding All loads of waste entering and exiting the site will be sheeted or otherwise contained Shredders only operate at slow and medium speed to prevent release of dust Dust suppression fitted to shredder and screener and mobile dust suppression units available for strategic positioning (i.e. loading areas, input area) dependant on need and level of dust created Speed restrictions on site All waste to be stored on hardstanding Visual inspection of dust levels on a daily basis | Low |
|  | Atmosphere | Habitats – Local Wildlife | Harm to nesting birds from dust deposition on food source | Medium | High | Low | Permitted wastes do not include wastes that solely consist of dusts, powders or loose fibres Shredding of waste wood has the potential to cause dust | Regular maintenance of all hardstanding All loads of waste entering and exiting the site will be sheeted or otherwise contained Shredders only operate at slow and medium speed to prevent release of dust Dust suppression fitted to shredder and screener and mobile dust suppression units available for strategic positioning (i.e. loading areas, input area) dependant on need and level of dust created Speed restrictions on site All waste to be stored on hardstanding Earth bund surrounding site minimises windblown dust leaving the site. Prevailing wind away from SSSI Visual inspection of dust levels on a daily | Low |
| Release of particulate matter (dusts) and micro-organisms (bio aerosols) | Atmosphere and then deposition | Local human population | Nuisance –dust on cars, clothing etc. | Medium | Medium | Low | As above | Regular maintenance of all hardstanding All loads of waste entering and exiting the site will be sheeted or otherwise contained Shredders only operate at slow and medium speed to prevent release of dust Dust suppression fitted to shredder and screener and mobile dust suppression units available for strategic positioning (i.e. loading areas, input area) dependant on need and level of dust created Speed restrictions on site All waste to be stored on hardstanding Earth bund surrounding site minimises windblown dust leaving the site. Prevailing wind away from SSSI Visual inspection of dust levels on a daily | Low |
|  | Atmosphere and then deposition | Habitats – SSSI (Down End Chalk Pit) | Damage to sensitive eco systems | High | Medium | Medium | Permitted wastes do not include wastes that solely consist of dusts, powders or loose fibres Shredding of waste wood has the potential to cause dust Deposition of dust on sensitive eco systems | Regular maintenance of all hardstanding All loads of waste entering and exiting the site will be sheeted or otherwise contained Shredders only operate at slow and medium speed to prevent release of dust Dust suppression fitted to shredder and screener and mobile dust suppression units available for strategic positioning (i.e. loading areas, input area) dependant on need and level of dust created Speed restrictions on site All waste to be stored on hardstanding Earth bund surrounding site minimises windblown dust leaving the site. Prevailing wind away from SSSI Visual inspection of dust levels on a daily basis | Low |
|  | Atmosphere and then deposition | Habitats – Deciduous Woodland | Damage to sensitive eco systems | High | Medium | Medium | Permitted wastes do not include wastes that solely consist of dusts, powders or loose fibres Shredding of waste wood has the potential to cause dust Deposition of dust on sensitive eco systems | Regular maintenance of all hardstanding All loads of waste entering and exiting the site will be sheeted or otherwise contained Shredders only operate at slow and medium speed to prevent release of dust Dust suppression fitted to shredder and screener and mobile dust suppression units available for strategic positioning (i.e. loading areas, input area) dependant on need and level of dust created Speed restrictions on site All waste to be stored on hardstanding Earth bund surrounding site minimises windblown dust leaving the site. Woodland is 300m to the SW of the site and Prevailing wind is away from this direction Visual inspection of dust levels on a daily basis | Low |
|  | Atmosphere and then deposition | Habitats – Local Wildlife | Damage to sensitive eco systems | Low | Medium | Medium | Permitted wastes do not include wastes that solely consist of dusts, powders or loose fibres Shredding of waste wood has the potential to cause dust Deposition of dust on sensitive eco systems | Regular maintenance of all hardstanding All loads of waste entering and exiting the site will be sheeted or otherwise contained Shredders only operate at slow and medium speed to prevent release of dust Dust suppression fitted to shredder and screener and mobile dust suppression units available for strategic positioning (i.e. loading areas, input area) dependant on need and level of dust created Speed restrictions on site All waste to be stored on hardstanding Earth bund surrounding site minimises windblown dust leaving the site. Visual inspection of dust levels on a daily basis |  |
| Release of litter | Atmosphere and then deposition | Local human population, livestock and Local Wildlife | Nuisances, loss of amenity and harm to animal health | Low | Medium | Medium | Local residents are often sensitive to litter | Regular maintenance of perimeter fencing All loads of waste entering and exiting the site will be sheeted or otherwise contained Nature of shred material is unlikely to contain wind blown litter Visual inspection of boundary on a daily basis Visual inspection of dust levels on a daily basis Implement litter picking duties as necessary | Low |
| Mud on Roads | Vehicles leaving site | Local human population and livestock | Nuisances, loss of amenity and road traffic accidents | Medium | Medium | Medium | Local residents are often sensitive to mud on roads. Road Safety | Regular maintenance of all hardstanding All loads of waste entering and exiting the site will be sheeted or otherwise contained Speed restrictions on site All waste to be stored on hardstanding or in bays Use of mechanical road sweeper as necessary. | Low |
| Odour | Atmosphere and then inhalation | Local human population | Nuisances, loss of amenity | Medium | Medium | Medium | Local residents are often sensitive to odour | Material being processed at the site is not odorous in nature Removal of wastes from site as soon as practicable to prevent accumulation | Very Low |
| Noise and vibrations | Atmosphere and ground for vibrations | Local human population | Nuisances, loss of amenity | Medium | Medium | Medium | Local residents are often sensitive to noise | All waste wood to be processed using slow and medium speed shredder Site situated within a sunken area that is bunded all around for attenuation Wood only processed during normal working hours Speed limits for vehicles Regular maintenance of hardstanding to prevent uneven surfaces All plant and machinery to be maintained in accordance with manufacturers specifications | Low |
|  | Atmosphere and ground for vibrations | Local Wildlife | Disruption to nesting | Medium | High | Medium | Noise and vibration can disturb the nesting patterns of birds | All waste wood to be processed using slow and medium speed shredder Site situated within a sunken area that is bunded all around for attenuation Wood only processed during normal working hours Speed limits for vehicles Regular maintenance of hardstanding to prevent uneven surfaces All plant and machinery to be maintained in accordance with manufacturers specifications | Low |
| Animals, Pests and insects | Atmosphere and land | Local human population | Nuisances, loss of amenity, harm to heath | Medium | Medium | Medium | Permitted wastes may attract scavenging animals Insects may arrive in waste load and multiply during favourable conditions i.e. summer months | Nature of waste wood does not attract scavenging animals as no putrescible element present Specialist contractor employed | Very Low |
| Spillage of leachate from waste, contaminated rainwater run-off | Direct runoff from site across ground surface via surface water drains | Surface water |  | Low | Medium | Medium | Site is not located in a flood risk area | Concrete hardstanding All run off drains to storage lagoon prior to removal by tanker Regular inspection of drainage system Regular maintenance of drainage system | Low |
|  |  | Groundwater |  | Low | Medium | Medium | Site is not located within a groundwater source protection zone | As Above | Low |