NEPTUNE CONTRACT SERVICES LIMITED ENVIRONMENTAL MANAGEMENT SYSTEM

Emergency Operating Procedures Reference: EMS-OP-02

NEPTUNE CONTRACT SERVICES Ltd. HUNDERER ROAD DAGENHAM RM9 6PU

Document Control Sheet

| Version Reference | Date | Reason for Change | Issued by |
| --- | --- | --- | --- |

CONTENTS

1	Introduction	1

1.1	Roles and Responsibilities	1

1.2	Purpose	1

1.3	Scope	1

2	Emergency Procedures	2

2.1	Fire Response	2

2.2	Spillage	2

2.3	Vandalism or unauthorised entry	4

2.4	Flood Warning and Evacuation Plan	5

Introduction

Roles and Responsibilities

The TCM has responsibility for ensuring these procedures are adhered to.  The TCM is specifically responsible for:

- Ensuring the adequate training of staff and contractors working on site regarding the content of these procedures;

- Ensuring the adequate provision of resources such as spill kits and personal protective equipment (PPE);

- Ensuring the provision and maintenance of hand held fine extinguishers at the site is adequate.

Purpose

The purpose of these procedures is to guide staff and contractors in the actions to be taken in the event of an emergency.

Scope

These Emergency Procedures are based on the Accident Management Plan set out in EMS-OP-01.

The scope of these procedures does not extend to health and safety related accidents such as personal injuries at work.  These are covered by the company Health & Safety procedures.

The contact list of emergency numbers in Appendix B will be retained in the Site Office and updated as required by the TCM.

Emergency Procedures

Fire Response

The Fire Plan is as follows:

Spillage

Potential causes of a spill

Minor spillages may be caused by:

- Machinery and fuel/oil leaks from vehicles

- Spillages or leaks from the diesel tank

Prevention of Spillages

Spillages and impacts from spillages will be prevented by:

- Controlling vehicle manoeuvring will be controlled

- Regular maintenance of plant and machinery

- Diesel tank to be double skinned and bunded

- Spill kits maintained in site office

Minor Spillage Procedure

A minor spillage is one that usually presents little or no risk to person or property, and is small enough to be safely cleaned up using the emergency spill kit.  The procedure is:

Spill Kits

Spill kits will be maintained at the facility in order to respond to any spill incident.  The spill kits will include:

- absorbent granules or sand;

- protective overalls;

- chemical/oil resistant gloves;

- chemical/oil resistant goggles; and

- a broom and shovel.

Major Spillage Procedure

A major spill is one that cannot be contained safely with the material on site and threatens safety to life and or the environment. The procedure is:

Vandalism or unauthorised entry

The site may be subject to unauthorised entry and vandalism which may pose a risk to environmental protection as well as health and safety.

If a staff member identifies evidence of unauthorised entry or vandalism they will:

Flood Warning and Evacuation Plan

Potential causes of a flooding

The site is located within an area not defended from flooding.

Flood Warning

The Site Manager will register with the Environment Agency for flood warnings

In the event of receiving a flood warning, the procedure is:

A copy of this procedure will be kept in the Site Office and Mess Facilities. All staff will be trained in this procedure.

Annex A: Emergency Contacts Register

| SITE DETAILS: NEPTUNE CONTRACT SERVICES LTD. |
| --- |
| Location: Thunderer Road, Dagenham |
| Postcode: RM9 6PU |
| Site Access Grid Reference: TQ 48342 82132 |
| SITE CONTACTS | Name | Office Hours (specify) | Out of hours |
| Owner: operator | Neptune Contract Services Ltd. | 0208-596-9880 | 07966 195105‬ |
| Director: | Mr. F. Fitzpatrick | 0208-596-9880 | 07966 195105‬ |
| Site Manager: | Mr. F. Fitzpatrick | 0208-596-9880 | 07966 195105‬ |
| Site Supervisor/Competent Person: | Mr. C. Benn | 0208-596-9880 | 07787 117449‬ |
| Security Contact: | Mr. F. Fitzpatrick | 0208-596-9880 | 07966 195105‬ |
| Landowner / Agent: | M. Long & Daughters Ltd. | 0208-596-9880 | 07966 195105‬ |
| EMERGENCY SERVICES | Office Hours | Out of hours |
| Emergency | 999 | 999 |
| Medical: Barking Hospital, Upney Lane, Barking IG11 9LX | 0203-644-2301 |  |
| Police: | 999 | 999 |
| Fire: Dagenham Fire Station, 151, Frizlands Lane, Dagenham RM10 7HD Barking Fire Station, Alfreds Way, Barking IG11 0BB | 999/0203-215-3000 0208-555-1200 | 999/01296-744400 0208-555-1200 |
| REGULATORS | Office Hours | Out of hours |
| Health and Safety Executive (HSE) | 0151 922 9235 | 0151 922 9235 |
| Local Authority: Barking & Dagenham Council | 0203-215-3000 | 0203-215-3000 |
| Environment Agency (Local) | 03708 506 506 | 03708 506 506 |
| EA (24 hour emergency hotline) | 0800 80 70 60 | 0800 80 70 60 |
| Natural England | 0845 600 3078 | 0845 600 3078 |
| UTILITY / KEY SERVICES | Name | Office Hours | Out of hours |
| Water undertaker: | Thames Water | 0800 316 9800 | 0800 316 9800 |
| Sewerage undertaker: | N/A |  |  |
| Gas supplier: | N/A |  |  |
| Electricity supplier: | N/A |  |  |
| Oil supplier: | N/A |  |  |
| Fuel supplier: | N/A |  |  |
| Chemical supplier: | N/A |  |  |
| Oil spill contractor: | N/A |  |  |
| Maintenance contractor: | In-house |  |  |
| Electrician: | In-house |  |  |
| Plumber: | In-house |  |  |
| Locksmith: | In-house |  |  |
| Joiner: | In-house |  |  |
| OTHER KEY CONTACTS | Name | Office Hours | Out of hours |
| Head Office: | N/A |  |  |
| Adjacent landowners: |  |  |  |
| Neighbours: |  |  |  |
| Neighbours: |  |  |  |
| Specialist advisors: |  |  |  |

Annex B: Staff Contact and Training Register

| Name | Job Title | Contact Telephone Number | Training Received (Insert Date) | Signature | In the Event of a Flood Warning, staff member has been notified (Date/Time and initial) |
| --- | --- | --- | --- | --- | --- |