Introduction
This Noise and Vibration Management Plan (NVMP) addresses the impact of noise and details the control measures implemented by Towens of Weston Ltd at their site in Westonzoyland to mitigate this risk. This NVMP will be stored within the EMS but also on site in the offices at Westonzoyland.

The NVMP addresses the impact of noise and the specific control measures required to mitigate the risk. These abatement measures will be implemented by the Site Manager to ensure that noise and vibration is controlled and does not affect the nearby receptors.

A Noise Impact Assessment was conducted in October 2017 by Wardell Armstrong to assess potential impacts (Appendix A). This management plan is written considering the comments made in the assessment.

This NVMP will be implemented on site to ensure it operates in accordance with:
- Integrated Pollution Prevention and Control (IPPC)
- Best Available Techniques (BAT)
- Chemical waste: appropriate measures for permitted facilities (EA guidance)

The noise management hierarchy for control should be to:
1. Prevent generation of noise at source by good design and maintenance.
2. Minimise or contain noise at source by observing good operational techniques and management practice.
3. Use physical barriers or enclosures to prevent transmission to other media.
4. Increase the distance between the source and receiver.
5. Sympathetic timing and control of unavoidably noisy operations.
Site Details
## Site Location
The site is located at Former Airfield, Land off A372, Westonzoyland, TA7 0JS (Figure 1). The approximate national grid reference for the site is ST 36201 34022. The site is located on an industrial park alongside multiple other commercial and industrial establishments. The nearest residential building sits 330 m north of the centre of the site.

Figure 1 – Site Location Plan

## Permitted area
The permit boundary is outlined in red on the site layout plan above.
## Waste operations on site
The site has an environmental permit under EPR/HB3004KS and a variation has been submitted to increase the tonnage allowance. HB3004KS permits the operation of physical treatment of non-hazardous waste (1.16.12) under the Environmental Permitting Regulations 2015.
Waste operations on site include the following:
- The loading and unloading of waste using mobile equipment
- The handling of waste by hand, excavators, front loading shovel and grab loaders
- Treatment of soils through the aggregate processing plant
- Crushing and screening of aggregates, soils and stones material
- Storage of non-hazardous and inert soils
- HGV’s and skip vehicle movements
The site will be managed in accordance with the site-specific Environmental Management System (EMS) and the non-hazardous and inert waste: appropriate measures for permitted facilities EA guidance (found on gov.uk).
The site operating hours are from 07:00 to 17:00 on Monday-Friday and 07:00 to 13:00 on Saturdays for core operations, waste deliveries and the collection of materials. There is no processing of waste material at the site on Sundays, during the night-time hours or on Public Holidays.
Any noise generating equipment will only be used during operating hours.
Crushing and screening will be conducted on a campaign basis only when an appropriate amount of material has built up to justify use of the machine. This will prevent the noise generating equipment from being turned on and off continuously throughout the day and therefore will reduce noise production. The on-time of machines is dependent on the amount of material on site which will be variable.
The equipment on site is as follows:
- Tracked 360° excavator x3
- JCB Telehandler
- Grab Loader
- Fixed Processing plant
- HGV movements
- Crusher / Screener
- Mini Digger
## Site Layout
The site comprises an open yard utilised for storage of waste soils, aggregates and WRAP products in open stockpiles and storage bays. Any non-conforming wastes are stored in the quarantine bays.
The site is enclosed within a 3m high concrete wall which acts as both a noise and dust barrier.
Vehicles enter on the east along the haul road off the A372 and pass the weighbridge, this is the sole entrance to the site. Loads are inspected from the office before being accepted on site. Once inspected wastes are tipped into the appropriate stockpile or storage bay. Vehicles follow the on-site one-way haul road and pick up products on their way out before again passing over the weighbridge and exiting on the eastern side of the site.
The office is located near the entrance of the site to allow observation of all vehicles entering and exiting the site.
Once materials are processed, they are transferred into their appropriate segregated outgoing bays to await collection.
The site will operate a crusher, screener and a processing plant. The processing will be carried out within the perimeter wall so activities should not produce fugitive noise emissions outside the site boundary. Measures outlined in this document and the Environmental Risk Assessment will be adhered to during processing activities.
Stockpiles are regularly managed to maintain their size and location on site. Crushing will be done in small volumes frequently to ensure that stockpiles remain below 3m and wind-whipping does not occur. This also prevents the need for the crushing plant to be operational for long periods of time.
The surface of the open yard and building is impermeable concrete. This creates a smooth surface for vehicles and HGVs to reduce noise from vehicle movements.
The perimeter concrete lego block walls and surrounding vegetation will act as a physical barrier to prevent noise escaping from site.
The site has designated one-way routes for the entrance/exit, allowing HGVs to move around the site to avoid the vehicles from disrupting and coming into contact with any materials in the waste reception and storage area. The site has been designed to minimise vehicle movements on site by having a one-way haul road so that vehicles can tip and load with minimal need to reverse and manoeuvre around the site. This reduces noise from vehicle movements and reversing alarms.

The site is located on an industrial park and is surrounded by other units and operating businesses. This will help with absorbing acoustics from the site to prevent noise leaving the site boundary.
Any sub-contractors hired onto site would be made aware of this NVMP and must adhere to the measures outlined in this document and the Environmental Risk Assessment. Noise suppression controls relating to the specific plant will be measured and controlled in accordance with the Part B permit issued by the local authority where the sub-contractor is based.
Noise Receptors
## Noise Receptors
An initial assessment was undertaken by MTS Environmental Ltd to identify all the receptors that may be sensitive to noise generated from the site within a range of 1000m. These are listed in Table 1 below alongside their relative distances from the site.
A receptor plan detailing the location of the receptors relative to the site is shown in Figure 2. The red line boundary indicates 1000m threshold area.

Table 1 – Noise receptors within 1000m of the Westonzoyland site
Receptor	Distance from site (m)	Direction
Residential
Caravan Park	155m	South East
Properties off A372	860m	North West
Manor Farm	900m	North
Springway Farm	260m	North
Property on Place Drove	670m	South West
Designated Land and Waterways
Site of Special Scientific Interest (SSSI) – Langmead and Weston Level	90m and 700m	South / South West
Local Wildlife Site - Weston Level	700m	South West
Priority Habitat Inventory (PHI) – Lowland Meadows	185m and further	South
PHI – Lowland Dry Acid Grassland	955m	South East
PHI – Coastal and Floodplain Grazing Marsh	40m	South
PHI – Deciduous Woodland	870m	East
Important Plant Areas Plantlife (GB)	90m	South
Higher Level Stewardship Target Area – Somerset Levels and Moors	0m	All directions
Pigditch Rhyne Network	145m	South and West
Sensitive Land Uses
Middlezoy Aerodrome	400m	East
Farm	115m	North West
Westonzoyland Allotments	680m	North West
Playing Field	700m	North West
Westonzoyland Airfield	450m	North
Control Tower	765m	North
Industrial/Commercial
Chard H J & Sons	100m	East
Kleen Kutt	264m	East
Bridgwater Motorcycle Training	590m	North West
Grandfields Westonzoyland Motor Track and Learner Driver Area	900m	East
T&K Motorcycle Training	910m	East
Hall G – Vehicle Repair	950m	North
Regency	170m	North East
Slabs R Us	210m	North
Public Rights of Way
Restricted Byway	90m	South West
Public Footpath	620m	South East
Infrastructure/utilities
A372	390m	North
Protected species
Priority Species - Curlew	0m	North and West
Priority Species - Lapwing	0m	All directions
Priority Species - Redshank	0m	North and West
Priority Species – European Water Vole	Up to 500m	All directions
Priority Species - Snipe	920m	West
Groundwater
The site is not within a source protection zone or drinking water safeguard zone

Figure 2 – Receptors within 1000m of the site

Thirty-two receptors are listed on the map, six of which are sensitive receptors for noise (highlighted in bold in Table 1): Caravan Park (Receptor 1), Springway Farm (Receptor 4), Langmead and Weston Level SSSI/LWS (Receptor 6), Pigditch Rhyne Network (Receptor 13), and four priority species (Receptor 31). The remaining receptors are low sensitivity receptors, all have been added to Figure 1 and the relative distances to the centre of the site detailed in Table 1.
Activities listed above could emit noise which could impair these receptors. However, with the control measures set out in this plan and the Environmental Risk Assessment, noise impacts will be effectively mitigated.
Noise could impact the road users on the A372 at Receptor 30, however limited noise will leave the boundary of the site with the implementation of the mitigation measures outlined in this plan. Due to the nature of this receptor which is a busy highway and a large source of noise itself, the site will not generate any noise levels above those produced by this receptor so will not affect users of the road here.
Receptor 13, the Pigditch Rhyne Network surrounding the south of the site have been classed as a sensitive ecological receptor as they are open watercourses with the closest located ~145m from the site. Noise has the potential to cause ecological stress within the animal community in the river. However, damage will be mitigated by the control measures set out in this management plan and the boundary wall between the site and receptor acts as a buffer for any noise that, in the unlikely event, escape from the site boundary. Any noise from the site will not be blown in the direction of the rhynes by the north easterly prevailing winds as the river is not located to the north east of the site.
Properties in the caravan park and Springway Farm (Receptors 1 and 4) are considered to be sensitive receptors as they are within 500m of the site. The properties in the caravan park and Springway Farm are not in the direction of the prevailing winds as they are located to the south east and north of the site, respectively. However, due to their proximity to the site, noise could have a negative effect on the residents. The site is surrounded by a 3 m high concrete lego block wall to act as a boundary against noise escaping the site. Alongside the mitigation measures outlined in this document and the Environmental Risk Assessment, any fugitive emissions and noise will be prevented from escaping the site boundary and impacting these receptors. Towens of Weston Ltd will also keep an open-communication channel with these receptors to ensure any issues with noise are corrected as soon as possible.
Other residential properties, Receptors 2, 3 and 5 are all located over 500m from the site. These receptors are unlikely to be susceptible to the adverse effects of exposure to any increased levels of noise due to their proximity. The distance between the site and the residences forms a potential buffer zone and allows time for noise to disperse before it could reach the receptors. Adding to this, noise will be mitigated from leaving the boundary of the site following the measures set out in this management plan.
Receptors 7-12, Priority Habitat Inventories, Important Plant Areas Plantlife and Higher Level Stewardship Target Area (Somerset Level and Moor), are considered ecological receptors. Members of the public using these sites for recreational purposes or plant/animal communities at these sites may be affected by increased noise. The mitigation procedures outlined in this plan will prevent any fugitive emissions from reaching these areas. The surrounding infrastructure of the site and perimeter wall will also act as a buffer to screen noise from reaching these receptors. No noise will be carried to the receptors on the prevailing winds as they are not located to the north east of the site, the prevailing wind direction.
There are two Sites of Special Scientific Interest (SSSIs) both named as Langmead and Weston Level, Receptor 6, located 90m south and 700m south west of the centre of the site. Weston Level is also a Local Wildlife Site (LWS) located 700m south west of the site. These are considered sensitive receptors as they are designated because of grasses and aquatic invertebrate. Natural England (NE) have been consulted. They acknowledge that the prevailing wind is in an opposite direction from the SSSI (Figure 3). As the areas are designated due to grasses, noise will not have a negative impact on the plant ecology here, however there may still be animals residing here which noise may affect. Noise, if arising at an impactful decibel, will be managed in accordance with our Environmental Management System, which covers this scenario.
There are three areas of priority species of birds (Curlew, Lapwing, Redshank) and one mammal priority species (European Water Vole) which cover the site location (Receptor 31) and one area of bird priority species for Snipe (Receptor 32) located 920m from the centre of the site. Noise is unlikely to spread to this receptor due to its proximity, but Receptor 31 is considered a sensitive receptor as it covers the site area. A general ecological impact assessment was conducted for the site and found that “No protected or invasive, non-native species of plant were identified and the habitats within the site which will be impacted by the proposed development were not deemed to provide critical resources for any other protected or notable species of animal.” Noise will be contained within the site boundary through the boundary wall and suppression measures outlined in this management plan so will not affect these species. The noise level from the site will not be above the existing level produced in the surrounding area. Communication with Natural England will be ongoing to ensure that any changes in the species whereabouts are known and appropriate additional measures are implemented.
Middlezoy Aerodrome (Receptor 14) and Westonzoyland Airfield (Receptor 18) are located 400m and 450m from the centre of the site but are not considered sensitive receptors as the nature of activity conducted there will not be impacted by excess noise. Noise may be carried to these receptors through high winds as they lie on the outskirts of the prevailing wind direction. However, noise will be contained within the boundary of the site through the boundary wall and mitigation measures outlined within this document and the Environmental Risk Assessment. Monitoring will be conducted on site daily at and outside the site boundary to ensure that no excess noise emissions are travelling off site and affecting these receptors.
There are multiple sensitive land uses surrounding the site (Receptors 15-17 and 19) which are considered medium risk receptors. Noise from the site could cause negative environmental and human health impacts at these receptors. However, with the mitigation measures outlined in this noise management plan, noise will be prevented from reaching the receptors. Due to the industrial uses of the surrounding area, this site will not generate more noise than the existing level at the location.
There are multiple industrial and commercial businesses located within 1000m from the site (Receptors 20-27). These are at a low risk due to the nature of the businesses and the fact that they are noise-generating themselves. The likelihood of noise being emitted from the site which would affect these businesses and the people involved is very low with the abatement measures identified within the Environmental Risk Assessment and this document.
There is one public footpath and a restricted byway located within 1000m of the site (Receptors 38 and 29). The footpaths are located on the opposite sides of the boundary wall and lines of trees. These both act as a barrier between the path and the site. Noise is unlikely to escape from the site and effect these paths due to its location surrounded by other industrial infrastructures and the abatement controls according to this Noise Management Plan.
There are many local wildlife sites, farmland and open spaces within 1000m of the site that are not marked on Figure 1. They are considered as low risk or low sensitivity in accordance with IAQM guidance. These have not been added as receptors to Figure 1.
## Environmental effects – Wind Direction
Wind rose data from Royal Naval Air Station Yeovilton, South Somerset show that the prevailing wind is on average only 3.9 m/s (8.8 mph) (a gentle breeze on the Beaufort Scale) to the North East, where winds of >5m/s occur ~3% of the time, which is considered infrequent (Figure 3). Winds from the west and north west blowing to the east/south east should also be noted as they are above 5 m/s but they occur less than 2% of the time. Winds of >5m/s from all other directions are defined as ‘infrequent’ occurring ~1% of the time.

Figure 3 - Wind rose data showing the average wind direction and strength at Yeovilton Meteorological station (source: Iowa Environmental Mesonet)

Yeovilton Meteorological weather station is located 21.6km from the site and has a similar topography and similar weather conditions. Therefore, this wind rose data is comparable to that of the site. This station was chosen over Weston-Super-Mare weather station, as it is located inland which is similar to the location of Westonzoyland depot as opposed to Weston-Super-Mare which is by the coast so will have different weather conditions.

Noise Impact Assessment
Wardell Armstrong were employed to undertake a Noise Impact Assessment for the site in Westonzoyland.
The data from this report is being used to support this NVMP. Wardell Armstrong surveyed noise at three locations representative of the existing sensitive receptors to the site. Noise monitoring was also undertaken at one location 5m from Towens similar existing site in Weston-Super-Mare. This data was used to provide source noise level data to inform the noise assessment report. Measurements of background noise levels were taken and assessed alongside measurements of ‘specific noise’ produced due to equipment associated with the proposed development.
The report assessed industrial noise in accordance with the British Standard 4142:2014 and British Standard 8233:2014.
The report assessed noise impact from activities carried out on the site in Westonzoyland including HGV movements, materials movement and crushing. Crushing operations will have the highest noise impacts.
Natural England were also consulted, and they provided the guidance that:
‘Natural England guidance currently suggests that birds begin to react to a noise level of above 55dB. As a general rule, if the noise source is no more than 3dB higher than background noise levels, then Natural England accepts that it is unlikely to be significant. However, knowledge of the site indicates low use of Langmead and Weston Level SSSI by SPA and Ramsar wetland birds, as potentially the land could offer supporting habitat to these European Site qualifying species.’
The noise monitoring was undertaken between 11:00 and 15:00 to capture background noise levels during the quieter periods of the day within the proposed operational hours of the development. An additional measurement was taken at approximately 5m from the crusher machine of a similar existing Towens waste transfer facility in Weston Super Mare in order to establish the likely worst case source noise levels of the proposed development. This was taken between 15:07 and 15:09 when traffic flows near the site were at their lowest.
During the survey, observations were made of the significant noise sources which contribute to the noise levels at the site and sensitive receptors, these include:
- Road traffic noise
- Industrial noise from Springway Lane Business Park
- Birdsong
- Other sources including distant aircraft, people talking and car doors
Potential noise levels of the site at Westonzoyland were assessed based on that from the crusher on their existing site, a worst case specific noise level was found to be 74 LeqdB(A). It is considered that levels will be lower than this for the majority of the time as crushing will only operate for 1-2 hours at a time.
Findings of the assessment show that the BS 4142 rating sound level will be equal to or lower than the background noise level at two of the receptors and is only +2dB at another receptor. This is defined as below a low adverse impact and the noise from the proposed development is unlikely to make the existing noise impacts at these receptors any worse. One receptor, Langmead & Weston Levels SSSI, showed a difference of +9dB meaning that noise from the proposed development is likely to have a fairly neutral effect at this location due to the existing residual sound level.
Noise levels from the proposed site will vary depending on the specific processing activity and there is potential for noise to escape but it has been assessed as causing a low impact on sensitive receptors with no mitigation measures in place, excluding the SSSI where it is found to have a moderate impact. However, with the mitigation measures (outlined below), this impact from noise on surrounding receptors from activities on site will be reduced.
Ambient noise levels at the SSSI is unlikely to exceed 55dB(A), thus complying with the Natural England guidance and the site will not cause a negative impact on birds through noise production.
The report concluded that with no mitigation in place there is likely to be a low impact on sensitive locations assessed. However, mitigation should be implemented to reduce noise levels at the SSSI. The report suggests that a 2.5m high concrete block wall along the south west site boundary can achieve the necessary mitigation to create a low impact site.

## Source – Pathway – Receptor Assessment

Table 2 - Source-Pathway-Receptor Routes
Source	Pathway	Receptor	Type of impact	Where relationship can be interrupted
Noise through vehicle movements on site	Air	Residential properties, businesses, SSSIs, LWS, habitats and rhynes	Intermittent noise disturbance during operating hours	Outlined in mitigation measures below
Noise and vibrations from the mechanical loading/ unloading of wastes	Air and vibration	Residential properties, businesses, SSSIs, LWS, habitats and rhynes	Intermittent noise disturbance	Outlined in mitigation measures below
Noise from treatment operations such as crushing and screening	Air and vibration	Residential properties, businesses, SSSIs, LWS, habitats and rhynes	Intermittent noise disturbance during operating hours	Outlined in mitigation measures below
Noise from the processing plant	Air and vibration	Residential properties, businesses, SSSIs, LWS, habitats and rhynes	Intermittent noise disturbance during operating hours	Outlined in mitigation measures below
Engine noise from loading shovel	Air	Residential properties, businesses, SSSIs, LWS, habitats and rhynes	Intermittent noise disturbance during operating hours	Outlined in mitigation measures below
Noise from reversing vehicle warnings	Air	Residential properties, businesses, SSSIs, LWS, habitats and rhynes	Intermittent noise disturbance during operating hours	Outlined in mitigation measures below

Noise Management and Control
## Noise Management Measures
The site has been designed to prevent noise production from vehicle movements on site with a one-way haul road so minimal movement around the site is required. Vehicles will access the site by using the existing access road off the A372 and enter on the west of the site, they will then exit to the west back onto the A372, thus reducing queueing of vehicle and reducing vehicle noise.
The internal haul road and access road have a speed limit of 10 mph and are surfaced with concrete producing a smooth surface, both of which reduces the noise from moving vehicles.
HGVs on site will use push alarms whilst reversing which are noise sensitive and quieter than regular reversing alarms. The loading shovel will use a broadband reversing alarm in place of a tonal reversing alarm.
When depositing material into storage bays, stockpiles or the processing area, drop heights shall be minimised.
Towens of Weston Ltd has an ‘Anti-Idling Policy’ for vehicles queuing for entry onto site or waiting to be serviced with materials which is enforced on site. Warnings will be given by site staff if drivers do not conform. Any drivers who continually do not conform will be prohibited from visiting the site in future. This will reduce the production of noise from vehicles waiting in a queue.
Towens of Weston Ltd has an informal ‘No Beeping Policy’ which is enforced for vehicles on site, it will be hand signal only.
 The site layout is designed to mitigate noise production. The processing plant is located in the north of the site, to give as much distance from the most sensitive receptor – the SSSI south of the site, this increases noise dispersion within the boundary of the site. The crusher is located towards the south west of the site. The boundary concrete lego block wall, storage of materials in walled bays and surrounding vegetation provide acoustic screening between noise sources and receivers. The site is screened from the SSSI by a high bank with tall mature scrub and trees, which is potentially also adequate to mitigate the effects of noise in average wind conditions.
Care will be taken when tipping materials to avoid noise from tailgate slamming. Formal warnings will be given to drivers who continually make tailgate noise when tipping, and they will be refused entry from site if they continue to produce unnecessary noise.
The site is surrounded by a 2.5m high perimeter concrete lego block wall. This acts as an effective acoustic barrier against vehicle and material movements on site. It will also contribute to blocking any noise produced from waste processing carried on the north easterly prevailing winds.

Storage bays are constructed concrete lego blocks which are absorbent to increase attenuation and prevent increased noise levels when material is dropped into bays.
Plant and machinery will work at a low engine speed to minimise noise output and regular maintenance will be carried out in accordance with manufacturer guidelines.
All plant and machinery will be switched off when not in use to prevent unnecessary noise production.
All staff will be sufficiently trained to use machinery and process material appropriately to produce minimal noise.

The site operating hours are from 07:00 to 17:00 on Monday-Friday and 07:00 to 13:00 on Saturday. The site will not operate on Sundays, Public Holidays or Bank Holidays unless for emergency maintenance. Waste processing which could be a potential source of noise will not start until 08:00, when background noise levels are higher, so that the impact is proportionately reduced and noise nuisance to nearby receptors is avoided.

The crusher is orientated away from the site boundary so that noise generated first spreads into the centre of the site to increase dispersion before it reaches the site boundary.

Processing activities like crushing will be done on a campaign basis and only be done once sufficient material has accumulated to avoid on/off use. The plant will not be in use constantly, it will typically be used for 1-2 hours a day and will only be used in daytime hours, thus minimising the production of noise from the site as this is the main source of noise.

The processing plant will be in operation from 8am – 4:30pm, the plant is in the north of the site at the furthest distance from the SSSI. The noise produced from the processing plant is not 3dB above the background noise. The lego block boundary wall acts as an appropriate acoustic barrier. Sensitive receptors are not affected by any noise produced by the processing plant.

Personal Protective Equipment (PPE) is made available to all site operatives. It is unlikely that noise and vibration from site operations will cause a nuisance to visitors to the site. However, all visitors shall be made aware that the site is a working processing plant.

All noise barriers and screening are implemented in accordance with Part 1 of BS 5228:1997.

Industrial noise from the existing site area is already present at the nearest receptor so Towens of Weston Ltd operations are unlikely to cause additional noise nuisance.
## Responsibility of Implementation of this Management Plan
All operatives will be made aware of the issue of noise and vibration on site and should be fully conversant with the contents of this Noise and Vibration Management Plan and other relevant documents.

The Technically Competent Manager (TCM) is responsible for the implementation of this NVMP.
The TCM will undertake daily sensory checks on all plant and operational activities.
Staff at all levels shall receive the necessary training and instruction in their duties relating to control of the plant and noise emissions. Training will be given to all operatives on all aspects and impacts relating to the operation.

The TCM will review the NVMP during annual audits to make sure it complies with the Environment Agency (EA) guidance. The NVMP will also be reviewed if any noise complaint is received.

## Noise Monitoring
The operator shall monitor emissions and make sensory inspections of operations; Table 3 sets out the measures for olfactory monitoring of noise.

Table 3 - Mitigation measures for noise emissions
Appropriate Measures for Reducing Emissions of Noise
Daily sensory monitoring of emissions at site boundaries shall be carried out by staff supervising all waste processing operations.	TCM to monitor operations throughout the day at and outside the site boundary that is downwind of operations in the north eastern corner of the site.
	Observations and weather conditions including wind direction will be recorded in the site diary.
	Complaints to be recorded in the site diary and complaint form.

Inspections should be carried out during daily operational hours, especially when carrying out activities that are noisy. Additional routine monitoring at and outside the site boundary downwind of operations will be carried out during noise-producing operations and when there are any third-party plant operational on site.

The operator shall record any abnormal observations in the site diary and report to the on-site TCM at the time of recognition who will review the monitoring. The records must include the time, location, and result of the sensory assessment. The records must be kept by the operator for at least two years and be made available to the regulator for examination, on request.

In an event that mitigation measures are not effective, and excessive noise escapes the site boundaries, all noisy activities should be suspended until investigation takes place to identify cause(s) and appropriate mitigation measures.

All site operations and processing will only be carried out during operational hours in the day and no site access will be possible out of hours. Therefore, no noise is expected to be produced out of hours.

Reporting and Complaints Response
## Engagement with the Community
A complaint form will be available for those who are affected by the operations. If necessary, a meeting shall be carried out with candidates if noise is causing a serious impact.
The site will have a publicly visible sign at the entrance with contact details for the Operator so neighbouring businesses or local residents can contact Towens of Weston if they have any complaints/issues.
This has been achieved through having an open-door approach so that any neighbours can visit the site and talk to site staff, any issues can be discussed and Towens will change procedures if appropriate to address the issue. This approach will be continued on the proposed site.
If required, Towens will hold a meeting with neighbouring businesses and local residents to discuss any changes on site and hear any concerns. Towens will be able to reassure the community that the site will not cause them any adverse issues as they will be following strict management systems (including measures set out in this document) to prevent any negative impacts.
In the event of an incident on site, all businesses and residents within 250m will be informed by a member of Towens staff by door-to-door visits.
## Reporting of Complaints
In the event of a complaint, the TCM will immediately investigate the source of noise and whether it is originating from the site. Appropriate measures should be made, and action will be taken to prevent any further excessive emissions leaving the site.
The complaint should be reported to the Environment & Compliance Manager and the Waste Director where it will be recorded. Should the concern be ongoing further investigations will take place to mitigate the effects on the receptor.
Towens should respond to the complaint within 10 working days, although mitigation should be in place as soon as is practically possible.
A Corrective Action Report will be completed describing the incident. A record shall be made in the site diary.
If deemed appropriate, the Environment & Compliance Manager will ensure that the Environment Agency (EA) is informed of these within 24 hours, ideally as soon as possible and as appropriate.

TCM will escalate investigations if successive complaints are received, operations will be suspended if 2 or more validated complaints are received within the same week. If complaints are found to be unsubstantiated, operations will continue at the discretion of the TCM.

## Management Responsibilities
The TCM shall take responsibility for any complaints.
To maintain good relationships with neighbouring residents, businesses and Natural England, Towens of Weston Ltd will ensure that:
- All neighbours know how to contact the site if they experience a noise and/or vibration nuisance. Contact details are clearly visible on the site notice board along with Environment Agency details.
- Any complaints are recorded and that problems, where possible, are addressed.

Any historical records kept off-site should be made available to the regulator for inspection within one working week of a request.

Any person having duties that are or may be affected by the matters set out in this NVMP shall have convenient access to a copy of this document and the permit. These documents will be available electronically via the Towens of Weston Management System and issued as hard copy.
Summary
Processes carried out at the Towens of Weston site in Westonzoyland may produce noise, but it will be limited by the mitigation measures. In any event, noise will not exceed recommended limits and will not cause nuisance to nearby receptors.

The main causes of noise will be related to waste processing activities and transportation.
Noise from processing activities will be controlled by effective site management with appropriate mitigation measures, this will include:
- A boundary concrete lego block wall to act as an acoustic barrier
- Waste processing plant located away from sensitive receptors
- Appropriate location of stockpiles, storage bays and site haul road
- Regular maintenance of all plant
- Limiting vehicle speed and procedures
- Careful transfer of material on site
- Design of site layout to reduce vehicle movements and reversing alarms

Daily monitoring of noise levels, a stringent complaints procedure and an annual review of the NVMP will be carried out to prevent any adverse noise impacts from the site.

The procedures outlined in this NVMP apply to all activities carried out at the Towens of Weston site in Westonzoyland.