Pre-application Report

Environmental Permitting (England and Wales) Regulations 2016

Pre-application Report

To: Steve Raasch (on behalf of A & C Turkeys Ltd)

Pre-application number: EPR/JP3047QP/A001

Deepdale Farm

Chetwynd

Newport

Shropshire

TF10 8BH

Date Completed 	– 27/09/22

Thank you for seeking advice before submitting an application for an Environmental Permit.

We have completed an initial ammonia screening assessment for your proposal to identify if you will need to submit a detailed modelling assessment with your application.

The screening assessment is based on your proposal to operate a farm which is permitted to stock 25,000 male turkey and 25,000 female turkey places.

Summary of the assessment:

The ammonia screening results carried out by the Environment Agency are only intended to apply to any EPR permit application and not for use in local council planning submissions.

Based on the information you have provided you will need to submit detailed modelling with your application. Further information about the screening results is provided in detail in Annex 1.

It will generally be necessary to employ experienced consultants to undertake this work. For more information about consultants you could contact your industry body representative or refer to the ENDs Directory:

http://www.endsdirectory.com/

A useful guide to choosing and using an environmental consultant can be found on the government's online resource for businesses ‘Business Link’:

http://webarchive.nationalarchives.gov.uk/20120823131012/http://www.businesslink.gov.uk/bdotg/action/detail?itemId=1079422318&type=RESOURCES

When completed, please include the detailed modelling report and supporting modelling files with your H1 Environmental Risk Assessment and submit these with your completed application form to the address given below.

For an example H1 Environmental Risk Assessment refer to the example Intensive Farming EPR application available on the national archives for Environment Agency Website:

http://webarchive.nationalarchives.gov.uk/20140328084622/http://www.environment-agency.gov.uk/business/sectors/40057.aspx

The Nature Conservation, Landscape and Heritage Factsheet screening lists all the sites that we currently consider when screening. The table details the supporting legislation and policies and the lead organisations for the protected area / species. Please note not all the sites listed are relevant to the Intensive Farming sector.

It is available on the Environment Agency website:

http://webarchive.nationalarchives.gov.uk/20140328084622/http://cdn.environment-agency.gov.uk/geho0612burd-e-e.pdf

Applying for your permit

You will need to complete application form part B3.5: https://www.gov.uk/government/publications/application-for-an-environmental-permit-part-b35

Your application should be emailed to:

PSC@environment-agency.gov.uk

or sent to:

Environment Agency Permitting and Support Centre

Environmental Permitting Team

Quadrant 2

99 Parkway Avenue

Parkway Business Park

Sheffield

S9 4WF

If you need further information about this screening assessment or applying for your permit please email us at the following address:

preapplicationservice@environment-agency.gov.uk

Pre-application nature conservation data are correct at the time of screening. We will consider all nature conservation sites using best available information at the time of permitting. Our GIS data are updated regularly, and we are occasionally made aware of additional nature conservation sites by other organisations which we will consider when determining a permit.

The Environment Agency takes care to ensure that the conclusions of the screening assessment are correct at the time of preparation but reserves the right to change the basis of the assessment in the light of technical developments or changes in Environment Agency procedures.

Annex 1 Ammonia Screening Results

Screening Input

Grid Reference used for the assessment: 371428, 323529 (with a 105m buffer)

Animal numbers and types

Animal numbers and types, housing systems, and manure storage assessed are listed below. The animal numbers and emission factors are based on an interpretation of the information provided by the applicant during the pre-application process and have been used in this initial risk assessment to identify if modelling is necessary.

It is strongly recommended that the numbers of animal places by category, ventilation type and housing system is reviewed, and appropriate emission factors are assigned before undertaking the detailed modelling assessment.

| Category of livestock | Housing system | Number of animal places | Ammonia emission factor (kg NH3/animal place/year) |
| --- | --- | --- | --- |
| Male turkeys | Fan ventilated fully littered floor, non-leaking drinkers Roof ventilation only (vents greater than 5.5 metres high, fan efflux velocity at or greater than 7 m/s)* | 25,000 | 0.45 |
| Female turkeys | Fan ventilated fully littered floor, non-leaking drinkers Roof ventilation only (vents greater than 5.5 metres high, fan efflux velocity at or greater than 7 m/s)* | 25,000 | 0.23 |

* this can include gable end fans that are used for heat extraction only during the summer months

Manure Storage – No manure stored on site

If you decided to alter your proposal by increasing the number of animal places or by changing the animal housing type or by increasing the manure storage you should include these changes in your modelling report.

Screening Overview

This screening assessment has considered any Special Areas of Conservation (SAC), Special Protection Areas (SPA) and Ramsar sites within 5km, any Sites of Special Scientific Interest (SSSI) within 5km and also any National Nature Reserves (NNR), Local Nature Reserves (LNR), ancient woodlands and Local Wildlife Sites (LWS) within 2km of the farm.

We have used the Environment Agency’s Ammonia Screening Tool (AST v4.6) to assess the impact of your proposal at those sites identified within the above distance criteria.

We have applied a two-stage screening criteria to the ammonia screening tool results:

For SAC, SPA, Ramsar and SSSIs the screening assessment has taken into account other intensive farms that could act in combination with the proposal, where applicable.

Where the ammonia screening tool predicts that emissions of ammonia or ammonia deposition (nutrient nitrogen or acid) will be <Y% (see Table 1 below) of the relevant Critical Level (CLe) (ammonia) or Critical Load (CLo) (nutrient nitrogen or acid), the proposal screens out of the requirement for an ammonia assessment.

Further modelling is required where:

- emissions of ammonia or ammonia deposition (nutrient nitrogen or acid) are in excess of Z% of the relevant CLe or CLo at SSSIs and/or other nature conservation sites (e.g. NNR, LNR, LWS, ancient woodland);

- emissions of ammonia or ammonia deposition (nutrient nitrogen or acid) are in excess of Y% of the relevant CLe or CLo for a SAC, SPA or Ramsar site;

- there is the potential for an in-combination effect with existing farms at a SSSI if emissions are > Y% of the critical level or critical load;

- the proposal is within 250m of a nature conservation site.

Table 1 Screening thresholds

| Designation | Y% | Z% |
| --- | --- | --- |
| SAC, SPA, Ramsar | 4 | 20 |
| SSSI | 20 | 50 |
| NNR, LNR, LWS, ancient woodland | 100 | 100 |

Screening Results

The Ramsar site listed in the table below requires detailed modelling as the emissions of ammonia is predicted to be > Y% of the relevant CLe. Detailed modelling is therefore required to assess the impact of airborne ammonia at the following site:

Table 2 Assessment of ammonia emissions

| Site Name | Designation / Status | Ammonia Critical Level (µg/m3) | Process contribution (PC) (µg/m3) | PC as % Critical Level |
| --- | --- | --- | --- | --- |
| Midland Meres & Mosses Phase 2 | Ramsar | 1 | 0.057 | 5.7 |

In addition to the above we have identified that there are existing permitted farms that could act in-combination with your proposal.

How we decided the sensitivity of the nature conservation site

Relevant Critical Levels were obtained from Natural England or the local wildlife trust or the local records centre or assigned using the best information available at the time from our internal mapping and data application.

Permitting Outcomes

For Ramsar sites a permit may be issued where either:

- the ammonia screening tool indicates that the process contribution is <4% Critical Level and Critical Load

or

- detailed modelling indicates the process contribution plus contributions from other relevant intensive farms is <20% Critical Level and Critical Load, AND additional checks* during determination are acceptable

or

- detailed modelling indicates the process contribution plus contributions from other relevant sources plus background is below the relevant Critical Level or Critical Load.

Please note (for Ramsar sites, where detailed ammonia modelling is required):

Following receipt of an application, determination may require an additional, more detailed assessment of the installation’s impact on the Ramsar site including, if appropriate, consideration of impacts of other local plans, projects, and non-permitted farms which could act in-combination. It may also include consideration of the condition of the Ramsar site and the background concentrations at the sites for ammonia, nitrogen deposition and acid deposition. This potential additional assessment is required to take into consideration recent case law.

The trigger level for completing the additional assessment during determination will be if the process contribution exceeds 1% of the critical level/loads. Following further detailed assessment, we may require the applicant to ensure ammonia emissions do not result in a process contribution at any Ramsar that exceeds 1%. We will contact the Applicant when duly making if we require any additional information to assess whether to grant/issue or refuse the permit.

Proposing ammonia emission reduction techniques

Where your modelling indicates the predicted process contribution is greater than the allowable thresholds your assessment and application should include ammonia reduction techniques* to reduce the contribution to the allowable threshold.

Where these criteria can not be met a detailed assessment of the proposal will be carried out by the Environment Agency. For Ramsar sites we will need to consult with Natural England before the determination of the application can be completed.

Factsheets and guidance about ammonia emissions to the atmosphere and nature conservation, the Environment Agency’s assessment process and how to model ammonia emissions from intensive farms can be found on our website at:

http://webarchive.nationalarchives.gov.uk/20140328084622/http://www.environment-agency.gov.uk/business/sectors/40071.aspx

*Please note: for Ramsar sites where additional checks are required during determination, further reduction of ammonia emissions may be required.