| Address: | Medisort Limited Hillingdon Clinical Waste Incinerator Pield Heath Road Uxbridge Middlesex UB8 3NN |
| --- | --- |
| Nature of Business: | Clinical Waste Treatment and Transfer |
| Date of Plan: | 04/07/2022 | Approved by: Stuart Brittle |
| Review Date: | TBA |  |
| Copies to: | Date Sent |
| Environmental Regulator: | Environment Agency |  |
| Fire Authority: | London Fire Brigade |  |
| Other: |  |  |
| Internal: | IMS Manual |  |

## 011.1 COMPANY CONTACTS

|  | Name |  | Mobile |
| --- | --- | --- | --- |
| Managing Director | Stuart Brittle |  | 07971 134 915 |
| Plant Manager | Mark Williams |  | 07714837468 |
| COTC Holder | Mark Williams |  | 07714837468 |
| Dangerous Goods Safety Advisor | Keith Harrington |  | 023 8070 2576 |

CONTENTS

011.1 COMPANY CONTACTS	1

011.2 EMERGENCY CONTACT DETAILS	3

011.3 SITE UTILITIES ISOLATION POINTS	3

011.4 SITE UTILITIES FAILURE	3

011.5 CORE PROCEDURE FOR THE PREVENTION AND MANAGEMENT OF ACCIDENTS	4

011.6 CHEMICAL, PRODUCT AND WASTE INVENTORY	4

011.7 FIRE IN THE HTTP BUILDING	5

011.8 PREVENTION OF DRAIN CONTAMINATION	5

011.9 HAZARDOUS WASTE SPILLAGE PROCEDURE	6

11.10 CLINICAL WASTE FLUID SPILLAGE	6

011.11 MINOR FUEL OR HYDRAULIC OIL SPILLAGE	7

011.12 SPILLAGE OF BOILER WATER TREATMENT CHEMICALS	7

011.13 BOTTOM ASH SPILLAGE	8

011.14 EVACUATION IN THE EVENT OF SPILLAGE OF CHEMICALS DURING WASTE OPERATIONS	8

011.15 RUPTURED STEAM PIPE OR STEAM LEAK	8

011.16 NEEDLE STICK INJURY	8

011.17 PERSONAL INJURY	9

011.18 FIRE WATER CONTAINMENT	9

011.19 FLOOD PLAN	9

011.20 EMERGENCY RESCUE PROCEDURE	9

011.21 CONTRACTORS AND VISITORS FIRE AND EMERGENCY PROCEDURE	10

011.22 CYTOTOXIC / CYTOSTATIC WASTE SPILLAGE PROCEDURE	10

011.23 RADIOACTIVE WASTE SPILLAGE PROCEDURE	10

011.24 GENETICALLY MODIFIED ORGANISMS (GMO) OR MATERIALS (GMM) WASTE SPILLAGE PROCEDURE	11

011.25 SPILL KIT CONTENTS	11

011.26 EMERGENCY PPE KIT CONTENTS	11

011.27 BUND MANAGEMENT PROCEDURE	12

011.28 BREACH OF SITE SECURITY	12

011.29 MUD AND DEBRIS ON THE PUBLIC HIGHWAY	13

011.30 OPERATOR ERROR	13

011.31 DUST FROM WASTE HANDLING OPERATIONS AND FROM TRAFFIC ON INTERNAL ROADS	13

011.32 FLOOR INSPECTION AND MAINTENANCE	14

DECLARATION	14

## 011.2 EMERGENCY CONTACT DETAILS

| Local Fire | Hillingdon Fire Station. 3-4 Uxbridge Rd, Uxbridge UB10 0PH |
| --- | --- |
| Local Police: | Hillingdon Police Station. 1 Warwick Place, Uxbridge, UB8 1PG |
| Local Hospital A&E: | Hillingdon Hospital. Pield Heath Road, Uxbridge, Middlesex, UB8 3NN Phone: 01895 238282 |
| Environmental Hotline: | 0800 807 060 (24hr Emergency hotline) |
| Environmental Regulator: | Environment Agency |
| Human Tissue Authority | 020 7269 1900 |  |  |
| IMPORTANT CONTACTS | Name |  |  |
| Local Authority: | Hillingdon London Borough Council |  |  |
| Sewerage Provider: | Thames Water |  |  |
| Water Supplier: | Thames Water |  |  |
| Gas Supplier: | British Gas. |  |  |
| Electricity Supplier: | SSE |  |  |
| Waste Management Contractor: | Veolia |  |  |

The following paragraphs define the procedures operators, and visitors must strictly follow in the event that the described incidents are discovered on the Site.

## 011.3 SITE UTILITIES ISOLATION POINTS

Fire Point Locations and Emergency Point Locations see site-specific drawing  D 003 Emergency Response

## 011.4 SITE UTILITIES FAILURE

Electrical power failure.

The Site's electrical supply is via the Hillingdon Hospital utilities infrastructure, which has its own emergency supply to which the Site is linked.

Loss of water supply

The Site has its water supplied via the Hillingdon Hospital utilities infrastructure, which is its own emergency supply to which the Site is linked.

Loss of burner fuel supply (Gas)

The Site's gas supply is via the Hillingdon Hospital utilities infrastructure, which has its own emergency supply which the Site is linked to.

## 011.5 CORE PROCEDURE FOR THE PREVENTION AND MANAGEMENT OF ACCIDENTS

The core procedure for the prevention and management of accidents defines the steps required to:

- Ensure all accidents, incidents, dangerous occurrences and emergencies are reported promptly, investigated and recorded accurately and that remedial actions are put in place where necessary.

- Ensure the company complies with the Reporting of Incidents, Diseases and Dangerous Occurrences Regulations (RIDDOR) and good practice with regard to the investigation of all incidents.

- The core procedure forms part of Medisorts Integrated Management System.

- Systems will be in place to communicate health and safety and environmental issues to all relevant staff and contractors in order to minimise the risk of accidents.

- All staff will receive training appropriate to their post to help minimise accidents. Records will be kept to ensure training needs are assessed and addressed.

- The Site will be audited on a regular basis; accidents and near misses will be investigated and the findings recorded. This information will be used to develop an improvement programme to prevent future accidents.

- Operating procedures include the safe shut down of the plant in an emergency.

## 011.6 CHEMICAL, PRODUCT AND WASTE INVENTORY

D002.1 WASTE STORAGE which includes Chemical Store

| Trade Name | Substance | Solid / liquid / gas / powder | Container size(s) | Maximum Quantity Held |
| --- | --- | --- | --- | --- |
|  | Hydraulic Oil | Liquid | 25 ltr | 250ltr |
|  | Diesel Engine Oil | Liquid | 205 ltr | 500ltr |
| AdBlue | Urea | Liquid | 205 ltr | 1000ltr |
| Antifreeze | Glycol | Liquid | 25 ltr | 100ltr |
| Screen wash | Alcohol | Liquid | 205ltr | 1000ltr |
| TFR | Traffic Film Remover | Liquid | 25ltr | 100ltr |
| Tornado | Detergent | Liquid | 205ltr | 1000ltr |
|  | Clinical Waste | Mixed | 770ltr | TBD |
|  | Anatomical waste | Solid / Liquid | 770ltr | TBD |
|  | Pharmaceutical | Mixed | 770ltr | TBD |

## 011.7 FIRE IN THE HTTP BUILDING

Person discovering the fire must:

- Immediately raise the alarm.

On hearing the fire alarm, the Fire Marshall must:

- Call the Fire Brigade by selecting a line and dialling 999, giving details of the fire;

- Attempt to fight the fire with fire-fighting equipment in the area only if it is safe to do so and the relevant training for fire extinguishers and fire fighting equipment has been given;

- Assess if there is any cytotoxic/cytostatic waste on Site. If so, advise the fire brigade and ask them to communicate with local residents to ask them to stay inside and close windows and doors.

- If there is any waste containing mercury, such as amalgam on Site, pull this into the yard if safe to do so.

On hearing the fire alarm, all other Personnel (including Contractors and Visitors) must:

- Report immediately to the fire-assembly point by the front door of the office.

Senior person at the fire-assembly point must:

- Take control of the situation and account for everyone;

- Consider sending someone to the site entrance to direct traffic and assist emergency services, as required.

All fires within the plant operations area must be reported to the Environment Agency by the Plant Manager

The Fire Assembly Point is located outside the front entrance to the office.

D003 LH Emergency Response HH shows the location of exits, assembly points, extinguisher positions and alarm components.

## 011.8 PREVENTION OF DRAIN CONTAMINATION

The Operator must:

- Use the appropriate procedure for the spillage (seek advice as appropriate);

- To prevent contamination of the sewer, the Operator must block the sewer outlet using the mat provided;

- Water in the interceptor should be monitored and diluted wherever possible and the contaminated water should be tankered away for disposal at a licensed facility.

NOTES:

In the event of a spillage or the situation of blocking or isolating the sewer outlet, the COTC Holder must be informed.

## 011.9 HAZARDOUS WASTE SPILLAGE PROCEDURE

Operator must:

- Immediately isolate the area

- Seal off drains

- Visually inspect the container that has spilled its contents for a label to identify the contents.

- If unsure on how to proceed, contact the Plant Manager for advice

- Put on appropriate PPE and carefully place all spilled material into a suitable container for disposal into the Autoclave, as directed by the Plant Manager.

- Clean up any spilled liquid using a mop and disinfectant.

- Wash down floor area.

- Complete an E005.4.1 Non-conformance Action Form.

Additional PPE

| PPE | Operator |
| --- | --- |
| Disposable dust mask | ( |
| Goggles | ( |
| Disposable coveralls | ( |

## 11.10 CLINICAL WASTE FLUID SPILLAGE

If personal contamination is suspected, the Operator must:

- Inform the Plant Manager or Supervisor of the spillage (if Operator must shower, someone else must inform the Manager or Supervisor);

- Wash/shower immediately, put on clean clothing; keep contaminated clothes separately from other work clothing (to await disposal);

If no personal contamination is suspected, the Operator must:

- Seal off drain

- Visually inspect the package for identification or warning labels;

- Never touch the package unless wearing appropriate PPE;

- If unsure on how to proceed, contact the Plant Manager

Dealing with a spillage

Plant Operator must:

- Contain any spillage, if safe to do so, but always before attempting to cleanup

- Cleanup the spillage using an appropriate absorbent agent, place spilled contents and packaging into a suitable container to await disposal in the plant or, as directed by the Operations COTC Holder

- Clean up any excess spilled liquid using a mop and disinfectant;

- Wash down floor area;

- Complete a E005.4.1 Non-conformance Action Form.

Additional PPE

| PPE | Operator |
| --- | --- |
| Disposable dust mask | ( |
| Goggles | ( |
| Disposable coveralls | ( |

## 011.11 MINOR FUEL OR HYDRAULIC OIL SPILLAGE

Operator must:

- On discovering a spillage, immediately inform Plant Manager.

- Isolate the source of the spillage;

- Block access into the drainage systems

- Protect the environment using absorbent granules to contain the spillage;

- Clean the contaminated area

Plant Manager must:

- Assess the severity of the incident;

- Determine any remedial actions to be taken, e.g.:

- Cordon off the spillage;

- Prevent unauthorised access to the area;

- Specify suitable sand/absorbent granules to contain the oil spillage;

- Instruct Operators to use sand/absorbent granules, sweep up the contaminated materials and place them into a one-way burn container, and to clean the floor with detergent to remove any fuel oil residues.

- Personally supervise the disposal of oil-contaminated absorbent material, ensuring that it is disposed of correctly

Additional PPE

| PPE | Operator |
| --- | --- |
| Disposable dust mask | ( |
| Goggles | ( |
| Disposable coveralls | ( |

## 011.12 SPILLAGE OF BOILER WATER TREATMENT CHEMICALS

The person who causes or finds a spill must:

- If the person who is filling the vessel gets contaminated, he/she should change work ware and wash up immediately;

- If inhalation or ingestion is suspected, the person must seek medical attention immediately

- If the spill is outside of the bunds, then the person who finds it must inform the Plant Manager; and block off drains using the drain mat;

- Isolated spill with contents of spill kit.

- Soak up spill with absorbent granules' or sand and place into a suitable container for disposal;

- after clean up wash down the area of the spill with copious amounts of water;

Plant Manager must:

- Personally supervise the disposal of chemical-contaminated absorbent material, ensuring that it is disposed of correctly

Additional PPE

| PPE | Operator |
| --- | --- |
| Disposable dust mask | ( |
| Goggles | ( |
| Disposable coveralls | ( |

## 011.13 BOTTOM ASH SPILLAGE

The person who causes or finds a spill must:

- Must inform the plant manager.

- Isolated the spill area.

Dealing with the spill. (Ashes)

- Sweep up the ashes or use the industrial vacuum.

- Transfer the ashes back into the ash skip or ash bags

- Wash down the area of the spill

Additional PPE

| PPE | Operator |
| --- | --- |
| Disposable dust mask | P |
| Goggles | P |
| Disposable coveralls | P |
| Gloves | P |

## 011.14 EVACUATION IN THE EVENT OF SPILLAGE OF CHEMICALS DURING WASTE OPERATIONS

- If a chemical spillage from the waste happens during any operation, the plant must be evacuated;

- The senior person on Site is to be informed immediately and all staff will report to the Fire Assembly Point;

- The senior person on Site will inform the COTC Holder by phone;

- The COTC Holder will assess the situation and deal with the problem with the senior person on Site or call out the Fire Brigade if deemed necessary;

- No person may re-enter the building until the COTC Holder or the emergency services gives the all clear.

## 011.15 RUPTURED STEAM PIPE OR STEAM LEAK

Senior person on Site must:

- In the event a steam leak or ruptured pipe is found during Plant start-up or normal operations the Operator must be instructed to stop the cycle at once

- The building must be evacuated of all non-essential personnel;

- The Senior person on Site must contact the Plant Manager and make him aware of the situation;

- The senior person on Site should monitor the situation until the Plant Manager arrives, if it is safe to do so.

The Plant Manager must:

- Arrange for repairs to be carried out by a suitably qualified contractor;

- Ensure that the Plant 'is' not restarted until full repairs have been completed, tested and signed off.

## 011.16 NEEDLE STICK INJURY

Injured person must:

- If the Needle is still in the skin, carefully remove it from the wound; and keep it in a single-use container

- If the Needle is not still in the skin, carefully find it without endangering anyone and do not touch it;

- Wear latex gloves and use the yellow forceps (in response kit) to place the needle/syringe carefully into the single-use container, lock it securely;

- DO NOT SUCK (OR LICK) THE WOUND;

- Encourage wound to bleed;

- Using the disinfectant wipe provided, clean wound, the area surrounding wound, and both hands,

- Place used latex gloves and wipes together with forceps into suitable container for disposal;

- Report accident to the Senior person on Site, and enter all details into the accident book located in the office;

- Report to local hospital and take needle with you.

In all circumstances the Senior Person must:

- Seek qualified medical advice if the injured person is feeling unwell.

Contact the appropriate department head to inform him/her of the incident.

## 011.17 PERSONAL INJURY

- Take appropriate action, e.g. First Aider, or Emergency Services;

- Inform the appropriate head of department

- Report all personal injuries and accidents, and record them without delay in the accident book that is kept in the company server;

- Employees must only return to work after injury is assessed and it is deemed safe to do so.

- Report all "near-misses" using forms provided so that action can be taken to prevent a recurrence.

## 011.18 FIRE WATER CONTAINMENT

In the event of a fire on the Site and only if safe to do so the Plant Manager or senior person on Site must isolate the drains using the drain covers or isolate the pumps to ensure that the fire water is contained on Site.

## 011.19 FLOOD PLAN

The Site is not in any recorded flood plain; however, if the Site does become subject to flooding, the operators must shut all doors and ensure that all waste bins are shut and locked. If the COTC Holder is not on Site he must be contacted. Sandbags will be made from the stock of on-site sand and confidential waste bags and placed around the doors. All waste must be transferred to the mezzanine, with priority given to pharmaceutical and mercury waste. The Environment Agency must be contacted and informed of the situation and asked for any advice. No site personnel must endanger themselves at any point. The moment a flood is noticed, all plant and equipment must be stopped, and the mains power switched off.

## 011.20 EMERGENCY RESCUE PROCEDURE

NO PERSON IS ALLOWED TO ENTER A CONFINED SPACE UNLESS SOMEONE ELSE IS STANDING BY THE ENTRANCE AND ALL PRECAUTIONARY MEASURES DETAILED IN THE CONFINED SPACE RISK ASSESSMENT HAVE BEEN COMPLETED.

In the unfortunate event that someone gets stuck or becomes unconscious inside a confined space:

- First, contact the emergency services;

- Send someone to the site entrance to direct the emergency services to the correct area;

- Contact the Plant Manager;

- Ensure that there is as much ventilation as possible (open all doors) around the area that the person is trapped in;

- Do not attempt to rescue the person until it has been deemed safe to do so.

## 011.21 CONTRACTORS AND VISITORS FIRE AND EMERGENCY PROCEDURE

- Leave by the nearest escape route (leave all tools and equipment where it is);

- Wait at the fire assembly point. Medisort personnel will hold roll-call;

- Inform Medisort personnel of any dangers that may be in the area you were working (i.e. Gas bottles or Chemicals);

- Do not return to the Plant building until the Plant Manager has given the all-clear.

The fire assembly point is located outside the office main entrance door.

## 011.22 CYTOTOXIC / CYTOSTATIC WASTE SPILLAGE PROCEDURE

Spill Management

- Contain the substance involved in the spill by covering with an impermeable plastic-backed pad.

- Cordon off the area. If possible, close off the area by closing windows and doors.

- Turn off any fans which may spread the spill/aerosols.

- Obtain the spillage kit.

- Identify Spill. Any spill should be identified with a warning sign so that other people in the area will not be contaminated.

- Put on required extra protective clothing.

Liquid Spills

- Cover the area immediately with thick absorbent pads or granules,

- Clean spill using dustpan and brush and place contents into one-way burn bin.

Powder Spills

If there is a powder spill, cover with a wet wad of paper towels and manage as liquid spill. Cover gently to avoid the spread of powder.

In all cases:

- Complete a E005.4.1 Non conformance Action Form.

- All used PPE must be disposed of as contaminated waste

| PPE | Operator |
| --- | --- |
| Gloves | ( |
| Disposable dust mask | ( |
| Goggles | ( |
| Disposable coveralls | ( |

## 011.23 RADIOACTIVE WASTE SPILLAGE PROCEDURE

Plant staff will isolate the spillage area and Contact the company RPS who will deal with the spillage

Liquid Spills

- put on the required PPE

- drop a handful of paper tissues on the spillage (do not mop around the area as this will spread the contamination)

- lift the damp tissues with tongs and dispose of the material in the radioactive waste bin

- work quickly but carefully to avoid exposure to ionising radiation

- repeat the process until the surface is dry

Solid Spills

- cover the area with "moist" paper tissues (wet wipes)

- proceed as for the liquid spill procedure above.

In either case, complete a E005.4.1 Non-conformance Action Form.

| PPE | Operator |
| --- | --- |
| Gloves | ( |
| Disposable dust mask | ( |
| Goggles | ( |
| Disposable coveralls | ( |

## 011.24 GENETICALLY MODIFIED ORGANISMS (GMO) OR MATERIALS (GMM) WASTE SPILLAGE PROCEDURE

Plant staff will isolate the spillage area and Contact the company RPS who will deal with the spillage

- RPS to contact the customer for confirmation of waste type and correct procedure to deal with the issue.

- Take photographs on your phone for evidence.

- Complete a E005.4.1 Non conformance Action Form.

| PPE | Operator |
| --- | --- |
| Disposable dust mask | ( |
| Goggles | ( |

## 011.25 SPILL KIT CONTENTS

There is a large 360ltr spill kit located on the Site at the reception door

Spill kit contents			Adjacent cleaning station

12 adsorbent pads			1 litter picker

Absorbent materials			1 Broom

1 dustpan and brush			1 Shovel

Checks must be made on a weekly basis to ensure the contents are correct

Depending on the content and nature of the spillage, use the appropriate container and disinfectant supplied on Site.

## 011.26 EMERGENCY PPE KIT CONTENTS

There will be 1 Emergency kit located on the Site

Typical contents for the Emergency kit;

- 2 pairs of safety goggles

- 1 pack of disposable gloves

- 2 pairs of chemical-resistant gloves

- Minimum 2 disposable chemical protection suits

- 1 box of FFP3 masks

Checks must be made at the start of each shift to ensure the contents are correct

## 011.27 BUND MANAGEMENT PROCEDURE

On a daily basis, the Supervisor will ensure that staff check all bunded areas are empty. This will include the

- All bunded palletised oils;

- Any stored liquid waste in containers.

Checks are to be carried out on all drip trays around the plant. Clean and repair any leaks found on plant or equipment. This will include:

- Hydraulic Packs

- Water pipe leaks.

Ensure that the drain inside the building is clear. If not, have it cleaned immediately. Findings from the inspection must be entered into the site logbook.

NOTE:

All spillages or leaks must be cleaned using the correct Spillage Procedure for the type of substance as detailed within this document

Report all leaks or spills to the COTC Holder and enter details onto the daily plant log

The Plant Manager will inspect areas to ensure checks are being done.

## 011.28 BREACH OF SITE SECURITY

- Hazardous waste will be stored in a secure building, minimising access by unauthorised personnel. Incompatible materials will be kept separately.

- The Site will be monitored by CCTV 24 hours a day, 7 days a week and all hazardous wastes will be stored and processed inside the building.

- The Site's perimeter fencing will be inspected weekly and any defects repaired as soon as practicable and in any event, within 5 days of discovery.

- Security gates will be located at the site entrance. The gates will be kept closed and locked should the Site be non-operational at any time.

- The gates will be inspected daily and any defect repaired as soon as practicable and in any event, within 5 days of discovery.

- In the event of access by unauthorised persons, security measures will be reviewed and upgraded where necessary.

## 011.29 MUD AND DEBRIS ON THE PUBLIC HIGHWAY

- The site entrance and internal roads are paved, and all waste storage and processing areas will be within a building and on a concrete pavement.

- Vehicles will not drive over unpaved surfaces or waste.

- The site entrance and internal roads will be maintained in good condition and will be laid to fall so that surface water will not accumulate.

- This will minimise the potential accumulation of mud and debris.

- The public highway, site entrance and internal roads will be inspected at least daily and any mud deposits removed by site personnel

- Site personnel will carry out weekly litter patrols of the Site and internal roads

## 011.30 OPERATOR ERROR

- The consequences of operator error, should it occur, could be harmful to site personnel, visitors, local residents, neighbouring workforces, groundwater, surface water, air quality and soils.

- In order to ensure the safe operation of the Site, employees and contractors working at the Site will be required to comply with the operator's Integrated Management System.

- Staff training will be provided to ensure that staff and contractors understand their roles and responsibilities.

- Waste management activities will be subject to control by a Technically Competent Person as part of the Fit and Proper Person requirement.

- As an additional measure, the waste processing will be controlled by an automated SCADA system.

- The SCADA system will be controlled from a central location and will be secured to prevent unauthorised access.

## 011.31 DUST FROM WASTE HANDLING OPERATIONS AND FROM TRAFFIC ON INTERNAL ROADS

- The consequences of a release of dust, should it occur, could be some harm to site personnel, visitors, local residents and neighbouring workforces.

- Wastes received in collection vehicles and closed containers will not give rise to significant dust release during delivery.

- The site entrance and internal roads will be paved, and all waste storage and processing areas will be on concrete pavement.

- Vehicles will not drive over unpaved surfaces.

- Daily checks will be made to ensure that the site surfaces are clean.

- The site entrance and internal roads will, when required, be kept clean by site personnel

See drawing D004 for drain locations.

- When the on call person arrives they will advise to the clean-up operation

## 011.32 FLOOR INSPECTION AND MAINTENANCE

The working area within the plant building is covered by 300mm thick, steel reinforced concrete slab.

- All floor areas must be checked on a Monthly basis. All damage must be reported to the Plant Manager.

- All plant staff must ensure that the roll-on-off storage containers are lifted off the floor and they are not dragged.

- The Plant Manager must seal off any damaged area and prevent waste from being stored on or close to the damaged area;

- He must arrange for all damage to be repaired as soon as possible,

Some areas of the floor have painted walkways which must be kept clear of any obstruction including waste storage. All expansion joints must also be checked to ensure that there is no damage.

## DECLARATION

I have read and understood the Accident Management Plan and signed the P101 Training Record