Climate change risk assessment worksheet: Trib of Derwent EPR/GP3101LS/A001

Potential changing climate variable	A Impact	B Likelihood	C Severity	D Risk (B x C)	E Mitigation (what you'll do to mitigate this risk)	F Likelihood (after mitigation)	G Severity (after mitigation)	H Residual risk (F x G)
1. Summer daily maximum temperature may be around 7°C higher compared to average summer temperatures now.	Ventilation system unable to maintain optimum temperature within livestock housing.	3	3	9	Keep a log of any hot days which occur each year. Install additional cooling system and upgrade building insulation.	3	1	3
2. Winter daily maximum temperature could be 4°C more than the current average.	No negative impact expected.	N/A	N/A	N/A	N/A	N/A	N/A	N/A
3. The biggest rainfall events are up to 20% more intense than current extremes (peak rainfall intensity)*.	a) Effluent treatment plant may require more capacity or careful management. b) Surface water drainage system overloaded. c) Wash-out of fines into watercourse. d) Overtopping of bunds.	a) 2 b) 3 c) 1 d) 1	a) 2 b) 1 c) 1 d) 1	a) 4 b) 3 c) 1 d) 1	a) Increase leachate storage capacity (can export to additional stores owned by JSR) b) Consider surface falls at design stage. c) Drains and lagoons managed. / d) The surface water management plan will need to take increases into consideration (bunds all have covers).	a)2 / b)2 / c)1 / d)1	a)1 / b)1 / c)1 / d)1	a)2 / b)2 / c)1 / d)1
4. Average winter rainfall may increase by 41% on today’s averages.	Surface water drainage system overloaded.	3	2	6	Additional surface water storage capacity. A significant amount of rainfall will be collected within the roof drains, to be drainage into the and transported into attenuation pond to end up in the River Derwent. Also, as above.	2	1	2
5. Sea level could be as much as 0.6m higher compared to today’s level*.	Inland site. Low impact expected.	3	2	6	Monitor permanent change to local river levels and plan for flood defences as appropriate.	2	1	2
6. Drier summers, potentially up to 45% less rain than now.	Increased dust – less water to suppress.	3	2	6	Additional surface water storage capacity (will also help mitigate higher rainfall).	3	1	3
7. The flow in the watercourses could be 40% more than now at its peak*, and 80% less than now at its lowest.	At low flow increased stress on the river at discharge point.	3	2	6	Manage the discharge flow rate to avoid impacts.	2	1	2