Environmental Risk Assessment

Farm name: Southlands Pig Unit	Operator: JSR Farms Ltd		Permit number:

Assessment of Odour Risk & Management

| What do you do that can harm and what could be harmed? | Managing the risk | Assessing the risk |
| --- | --- | --- |
| Hazard | Receptor | Pathway | Risk management | Probability of exposure | Consequence | What is the overall risk? |
| What has the potential to cause harm? | What is at risk? What do I wish to protect? | How can the hazard get to the receptor? | What measures will you take to reduce the risk? If it occurs, who is responsible for what? | How likely is this contact? | What is the harm that can be caused? | What is the risk that still remains? The balance of probability and consequence |
| Odour from feed mixing, delivery and storage | JSR Owned House within 400m | Air | Measures as described in ‘How to comply with your environmental permit for intensive farming V2 Jan 2010’ (EPR 6.09 Sector Guidance Note) Odour Management Plan in place Feed delivery will be sealed to minimise atmospheric dust. Any spillage of feed around the bin is immediately cleaned up. The condition of feed bins is checked frequently so that any damage or leaks can be identified All feed ingredients are stored in covered tanks The unit is relatively isolated so there is minimal risk of dust causing direct odour nuisance | Unlikely | Odour annoyance | Not significant |
| Odour arising from problems with housing ventilation system Inadequate system design causing poor dispersal of odours. | JSR owned house within 400m | Air | Measures as described in ‘How to comply-Intensive Farming’. The ventilation system is automatic and regulates heating and ventilation to achieve optimum environmental conditions. The ventilation system will be designed to efficiently remove moisture from the house. Buildings with higher ventilation rates (vents greater than 5.5 metres high, fan efflux velocity greater than 7m/s) will discharge exhaust air via roof vents for improved dispersal. Stocking density maintained at or below levels set out in Welfare Regulations. | Unlikely | Odour annoyance | Not significant |
| Manure and slurry management: Odours arising from poorly managed slurry collection, removal and distribution Spillage of water from drinking systems Disease and vice outbreaks | JSR owned house within 400m | Air | Measures as described in ‘How to comply-Intensive Farming’ Controls on feed and ventilation (see above) help to maintain air quality Additional controls include: Insulated walls and ceilings to prevent condensation Regular maintenance and correct positioning to avoid overflow from feed and drinking systems Stocking density at optimal levels to prevent overcrowding Pens and yards kept clean Frequent removal of slurry; wind direction observed | Unlikely | Odour annoyance | Not significant |
| Carcase disposal: Inadequate storage of carcases on site | JSR owned House within 400m | Air | Measures as described in ‘How to comply-Intensive Farming’ Carcases removed from the pig building and are disposed of in accordance with the current Animal By-Products Regulations, with a licensed incinerator on site. All odour complaints are logged and investigated | Unlikely | Odour annoyance | Not significant |
| Buildings: Cleaning and disinfection Emptying slurry pits |  | Air | Pens and yards kept clean Frequent removal of manure and slurry, wind direction observed Potentially odorous spillages cleaned up promptly | Likely | Odour annoyance | Not significant if carefully managed |
| Odour arising from slurry spreading | Neighbouring dwelling houses within 400m of spread sites | Air | As above Slurry exported to JSR arable land for utilisation Any which is land-spread is highlighted in the manure management plan and also follows NVZ rules Intermittent activity only | Likely | Odour annoyance | Not significant if carefully managed |
| Odour arising from manure and slurry. Storage – dirty tanks, slurry tank/lagoon | Neighbouring dwelling houses within 400m of spread sites | Air | Site will operate under odour management plan Feed selection to minimise excretion of nutrients. Storage areas sited away from neighbours Areas of open, dirty concrete minimised Stores regularly emptied | Likely | Odour annoyance | Not significant if carefully managed |

Table 2 Assessment of Noise Risk

| What do you do that can harm and what could be harmed | Managing the risk | Assessing the risk |
| --- | --- | --- |
| Hazard | Receptor | Pathway | Risk management | Probability of exposure | Consequence | What is the overall risk? |
| What has the potential to cause harm? | What is at risk? What do I wish to protect? | How can the hazard get to the receptor? | What measures will you take to reduce the risk? If it occurs – who is responsible for what? | How likely is this contact? | What is the harm that can be caused? | What is the risk that still remains? The balance of probability and consequence |
| Noise problems from large vehicles travelling to and from the farm. Mobile source | JSR owned house within 400m | Air | Measures as described in ‘How to comply-Intensive Farming’ Vehicles are required to be driven on to and off site with due consideration for neighbours Deliveries of feed and fuel are made only during the daytime, if possible, so that disturbance is minimised General animal movements made during working day hours and with minimum stress All vehicles maintained so as to minimise engine noise and are driven slowly to and from the site Roads and tracks maintained to minimise noise produced | Unlikely | Noise annoyance | Not significant if managed carefully |
| Large vehicles on site for delivering feed, loading live pigs at end of the growing period, removal of slurry from houses Mobile source | JSR owned house within 400m | Air | Measures as described in ‘How to comply-Intensive Farming’ Vehicles have to be well maintained and must be driven slowly around the site Engines to be switched off when not in use Vehicles which are fitted with an audible warning system are generally used only in the daytime Idling of machines avoided and engine revs kept low Slurry tanker filling and emptying done as an intermittent activity Machinery and equipment sited as far as possible from neighbours | Unlikely | Noise annoyance | Not significant |
| Small vehicles travelling to and from the farm eg staff and visitors’ cars, courier van deliveries, etc Mobile source | JSR owned house within 400m | Air | Measures as described in ‘How to comply-Intensive Farming’ Small vehicles arrive during the normal working day and therefore are seen as low risk | Unlikely | Noise annoyance | Not significant |
| Feed transfer from lorry to bins and tanks Fixed source | JSR owned house within 400m | Air | Vehicles are well maintained and designed so that noise during feed transfer is minimised Conveyors and augers not operated when empty | Unlikely | Noise annoyance | Not significant |
| Operation of fans Fixed source |  | Air | Efficient extractor fans used and maintained in good condition to avoid excessive noise Forced ventilation systems with automated controls to minimise run time and fan speed | Unlikely | Noise annoyance | Not significant |
| Pigs Mobile source |  | Air | Noise from pigs may be considered to be a likely cause for complaint During loading, noise from animals is minimised by careful handling and by prompt removal of the lorry from the site when full | Unlikely | Noise annoyance | Not significant |
| Personnel Mobile source |  | Air | Staff and other contractors are required to carry out their work without creating excessive noise from shouting and use of radios, etc | Unlikely | Noise annoyance | Not significant |
| Repairs |  | Air | Noise Management Plan in place If repairs to the site are required, the work is undertaken with due regard for possible noise nuisance and during the normal working day In the event of major repair work being undertaken which is likely to cause significant noise and disruption, neighbouring residents will be notified in advance | Unlikely | Noise annoyance | Not significant |
| Slurry spreading | wildlife | Air | Machinery operated at reasonable times where possible and idling avoided Equipment maintained to optimum standards | Likely | Noise annoyance | Not significant if managed carefully |

Table 3 Assessment of Fugitive Emissions Risk

| What do you do that can harm and what could be harmed | Managing the risk | Assessing the risk |
| --- | --- | --- |
| Hazard | Receptor | Pathway | Risk management | Probability of exposure | Consequence | What is the overall risk? |
| What has the potential to cause harm? | What is at risk? What do I wish to protect? | How can the hazard get to the receptor? | What measures will you take to reduce the risk? If it occurs – who is responsible for what? | How likely is this contact? | What is the harm that can be caused? | What is the risk that still remains? The balance of probability and consequence. |
| To air |  |  |  |  |  |  |
| Dust (including bio aerosols) Sources: Feed Incinerator ash | Farm House Nuisance Contributes to odours Human health (inhalation) Surrounding vegetation: Covers leaves and inhibits photosynthesis Surrounding land: Nutrient enrichment of soils Contributes to respiratory problems for pigs and staff | Air | Use of meal feed delivered in sealed systems and stored in covered containers. Mainly wet fed to pigs, reducing the release of dust. Control fed, so minimised waste and feed not left to ferment in the troughs which would create odours/emissions. Regular clearing of dust to prevent build up within buildings, on roofs and around vents, as part of efficient ventilation systems Incinerator ash kept sealed within incinerator before being added to slurry for application to land. | Management actions should prevent this happening | Nuisance: dust on surrounding vegetation, cars, clothing Smothering and direct damage to nearby vegetation Pigs/staff may get stressed and become unwell | Not significant if managed carefully |
| Ammonia Source: Pig housing and manure/slurry/dirty water storage, removal and spreading | JSR owned house within 400m Pigs and staff: high levels can cause respiratory problems Also perceived as a nuisance as it contributes to odours Surrounding vegetation: direct toxic effect and changes to sensitive ecosystems Surrounding land: Nutrient enrichment and acidification of soils | Air | Measures as described in ‘How to Comply – Intensive Farming’ Mitigation measures as for odour Feed formulated to match pig requirements and to minimise amount of ammonia produced Rations under periodic review Ventilation and control systems designed to provide optimal environment and regularly monitored and maintained Covered slurry store fitted with double gate valves Regular monitoring of tank and store contents and maintenance of facilities and equipment Frequency of slurry removal to minimise ammonia emissions Dedicated purpose built facilities for slurry and dirty water Slurry spread at low level and in accordance with the Manure Management Plan and NVZ rules Fully trained operators Soils regularly analysed and applications made in response to crop requirements to avoid spreading more slurry/manure than is needed, under JSR Arable Farms | The impact of ammonia on air emissions from the installation has been assessed in the pre-application with conclusions of no need for further modelling | Aerial deposition and direct toxic effect on trees Nutrient enrichment of soils and changes to sensitive ecosystems Respiratory problems in humans and mammals | Not significant |
| Zoonoses and notifiable diseases | Human health and livestock health | Air/direct contact | Detailed biosecurity precautions in place, eg frequent stock inspection, use of disinfectants and appropriate clean overalls, boots, etc for staff, visitors and contractors, to prevent spread of disease Secure site visitor policy Livestock monitored for signs of disease and incidents reported quickly Use of a health plan, with specialist veterinary input in place. | Unlikely | Human and livestock health implications | Not significant if managed carefully |
| To water |  |  |  |  |  |  |
| Nutrients such as N and P plus organic matter Source: Wash water run off to nearby water course, muck and slurry spreading | Adjacent Water Course: Nutrient leaching from soil to surface waters and groundwater, causing eutrophication and increased biochemical oxygen demand (BOD) of watercourses | Land | Dirty water runoff is diverted to under-slat slurry pits (should be very limited surface water due to the area being fully concreted). Feed spillage on yard/roadways during clean out is cleaned up Manure management plan followed including NVZ rules for spreading slurry, under JSR arable Farms | Unlikely | Pollution of groundwater leading to eutrophication and poisoning of flora and fauna | Not significant if managed carefully |
| Spillages from storage and use of pesticides and fuel/chemicals | Vulnerable groundwater beneath site | Land | Management techniques employed aimed at avoiding minimising use where possible Use of approved chemicals only Operators fully trained and all equipment regularly maintained to avoid any in-field spillage or discharge All fuel tanks bunded and compliant with legislation | Unlikely | Contamination of groundwaters Killing of flora and fauna | Not significant |
| To land |  |  |  |  |  |  |
| Ammonia from storage of dirty water, slurry, manure and housing | There is not an SSSI within 500m of the new site and was no site identified in the pre-application as an area of risk. | Air | As for odour and ‘To water’ above Feed selected to minimise excretion of nutrients Storage sites sited away from sensitive receptors Slurry store covered | Likely | Direct toxic effect on trees, nutrient enrichment and acidification of soils Changes to sensitive ecosystems . | Not significant if managed carefully |
| Waste materials, packaging, etc. Source: Non-organic waste storage and disposal | Neighbouring dwellings and surrounding habitats and countryside | Air | Policy to avoid production where possible Dedicated storage areas and facilities Collected by licensed contractors for re-cycling or disposal Regular checks made for rubbish dumped by third parties | Unlikely | Amenity value of countryside spoilt by rubbish Possibility of causing harm to wildlife | Not significant |
| Pests |  |  |  |  |  |  |
| Flies on manure heap could move off-site and affect nearby residents Also, birds, rats, etc. | Neighbouring dwelling houses | Air | Food sources covered and secure from pests Pest control programme in operation | Unlikely | Flies and rats are a vector of pollution that can harm human health Concerns about this pollution can cause offence and affect amenity | Not significant if managed carefully |

Table 4 Assessment of Accident Risk

| What do you do that can harm and what could be harmed | Managing the risk | Assessing the risk |
| --- | --- | --- |
| Hazard | Receptor | Pathway | Risk management | Probability of exposure | Consequence | What is the overall risk? |
| What has the potential to cause harm? | What is at risk? What do I wish to protect? | How can the hazard get to the receptor? | What measures will you take to reduce the risk? If it occurs – who is responsible for what? | How likely is this contact? | What is the harm that can be caused? | What is the risk that still remains? The balance of probability and consequence. |
| Spillages from pesticide and biocide handling and storage areas escaping | Potentially polluting liquids flow over yard to surrounding land and vulnerable groundwater beneath site | Flowing over yard or through cracks in poor impermeable surface and through the ground | Accident Management Plan in place Repair any infrastructure and design appropriate containment measures Maintenance and regular inspection procedure designed and implemented Foot dips on good concrete with drains or will be emptied into underslat pits and are located where overflowing gutters will not dilute Regular inspection of facilities and records kept Dedicated container for storage with impermeable hard standing within bund Removed from site by licensed contractor Damaged or suspect packaging rejected at time of delivery | Very unlikely | Contamination of local groundwater and potential nearby abstractions | Not significant with measures indicated |
| Spillage of slurry and feed due to operator error when loading and unloading | Land, groundwater | Land, groundwater | Standard operating procedures applied for loading and unloading Any spillage of feed around the bins and tanks is immediately cleaned up using materials which are stored nearby Area drains to slurry store so containment provided The condition of feed bins and tanks is checked frequently so that any damage or leaks can be identified in accordance with the site maintenance and inspection procedure Levels measured to prevent overfilling and sight gauge enclosed Barriers are in place to prevent collision All suppliers are supervised while on site Fully trained operators | Unlikely | Contamination of groundwater | Not significant |
| Failure to contain firewater or off-site pollutants | Groundwater |  | Accident Management Plan in place Off site pollutants, contaminated water will run into the slurry reception pit. | Unlikely | Contamination of groundwater and surrounding land | Not significant |
| Incorrect disposal of wash water | Soakaways | Land | Staff trained in correct operation procedures | Unlikely | Contamination of ground water | Not significant |
| Acts of vandalism which cause damage to structures and fittings | Surrounding land, ground waters | Land, water | Site security | Low | Contamination of soil and or water | Low |
| Flooding and other storm damage | Surrounding land, ground waters | Land, water | Good site layout and design Maintenance of site infrastructure and local flood defences Observe weather forecasts and weather warnings | Low | Water and soil pollution | Low |
| Power outage causing failure of slurry pumping systems resulting in tank overflow Failure of automatic liquid level control sensors and devices | Surrounding land, ground waters | Land, water | Stand-by generator | Low | Overflow of storage facilities | Low |
| Fire | Livestock, staff, buildings, fuel and oils, chemicals, bedding, feed, local habitats and neighbouring dwellings | Air | Regular inspection and maintenance of equipment | Unlikely | Toxic smoke and other pollutants, surface run-off from firefighting water, surface run-off from failed storage tanks, pipes and stores Exploding fuel containers Increased numbers of dead animals for disposal | Low |
| Below ground dirty water tank and pipe ruptures/overflows (including used disinfectant) | Dirty water flows over yard to clean drain inlet at the back of the office and into local water course | The surface water drainage system | Use of Defra/NOAH approved disinfectants Contact office or duty manager. If necessary contact Environment Agency | Unlikely | Contamination of groundwater | Not significant |